Note:  Reviewers: Adjust described areas for each job.  Accept the changes for jobs with repairs to the slab overhang and rejects the changes when no repairs to the slab overhang is to be performed.

CLEAN AND EPOXY SEAL			2/9/16

1.0  Description.  In order to protect the bridge superstructure concrete from deicing chemicals and other contaminates, loose and delaminated concrete shall be removed and an epoxy seal shall be applied to the concrete in the area of curb outlets and the vertical face of the curbs in accordance with the bridge plans and this job special provision.

2.0  Construction Requirements.  After repairs to the slab has been performed and the concrete fully cured as required by the epoxy manufacturer’s written recommendations, the epoxy sealing preparation and applying the epoxy to these areas shall be in accordance with Sec 704.  The areas to be cleaned and epoxy sealed shall be as follows:

(a)  Deck surface and vertical faces inside the curb outlets.

(b)  Outside edge of the deck to 12 inches on each side of the curb outlets.

(c)  Superstructure concrete area directly below the curb outlets from the edge of the deck to the edge of the top flange of the girder and to 12 inches on each side of the curb outlets.

(d)  Vertical face of the curbs for the entire length of the bridge.

3.0  Method of Measurement.  The area to be cleaned and epoxy sealed will be computed to the nearest square foot.  Final measurement will not be made except for authorized changes during construction or if appreciable errors are found in the contract quantity.

4.0  Basis of Payment.  Payment for the above described work, including all material, equipment, labor and any other incidental work necessary to complete this item, will be based on the contract plan quantities and will be considered completely covered by the contract unit price for “Clean and Epoxy Seal”.  Any change in the contract plan quantities, based on approved change orders, will be paid for at the contract unit price.