## Slide 1: Advanced Work Zone Training
Course Code: 24509

## Slide 2
Contents
Section 1: Overview
Section 2: Planning the Work Zone
  2A: Who will be Driving Through Your Work Zone
  2B: Work Zone Considerations
  2C: Night Work Considerations
Section 3: Device Selection & Quality Requirements
  3A: Site Preparation & Work Zone Set-Up
  3B: Protective Vehicle/TMA
Section 4: Flagging Operations
Section 5: Work Zone Inspections
Section 6: Safe Work Zone Removal Principals
Section 7: Post Work Zone Debriefing

## Slide 3
Section 1: Course Overview
Notes: Purpose of this section 1 is to review basic work zone principles, and to review the standards of work zone setup/design.

## Slide 4: Who Needs to be Trained?
Each person whose actions affect temporary traffic control zone safety, from the upper-level management through field workers, should receive training appropriate to the job decisions each individual is required to make.
MUTCD 2009 and Work Zone Safety and Mobility Rule Making 2004
Notes: Explain:
All employees, whose actions affect work zones, will be trained. MoDOT employees will receive this course, and employees who design more complex work zones will receive additional training relevant to their job
This is from the MUTCD Manual Part 6 December 2003

## Slide 5: Goals of the Work Zone
Zero Work Zone Fatalities
Reduce All Work Zone Crashes
Traffic Delays of 15 Minutes or less
Provide customers with real-time work zone information
Provide a reasonably safe environment for workers and public
Notes: Safety is our #1 Value for workers, motorist and pedestrians when exposed to or in a work zone.
A properly designed and executed temporary traffic control plan will enable the temporary traffic control zone to provide the above noted functions in the most effective manner possible

## Slide 6: Tracker
Reports quarterly on ability to provide safe, effective, and efficient work zones
Performance Measures
Percent of work zones meeting expectations

## Slide 7: How to Reach Our Goals
Provide safe and efficient movement of traffic
    Motorized
    Non-Motorized
Provide protection for workers and equipment in the workspace
Notes: Think about bicyclist and pedestrians as well.

## Slide 8: How do we make work zones safe?
By following:
Standards of Quality
Consistency
Part 6 of the MUTCD sets forth the minimum requirements for any utility or permit work on our state highways.
The MUTCD:
Sets minimum standards
Provides guidance
Ensures uniformity
Helps reduce cost of TCDs
Notes: Traffic control devices are critical for the safe and efficient transportation of people and goods. The use of uniform TCDs helps reduce crashes and congestion and improves the efficiency of the surface transportation system. Uniformity helps reduce the cost of TCDs through standardization. Key factors to designing a temporary traffic control plan should, provide positive guidance, be sensitive to the road user’s needs, minimize congestion and delays.
Easy to reference for crews working within the scope of utilities and permits.
Some flexibility for certain devices and equipment as long as they comply with the MUTCD
Click on “MUTCD” hyperlink for full overview.

## Slide 9: MUTCD
National standards governing all traffic control devices (TCDs)
Law governing all TCDs
Maintains Uniformity
Notes: The MUTCD defines the standards used by road managers nationwide to install and maintain traffic control devices on all public streets, highways, bikeways, and private roads open to public travel. It is a compilation of standards for all devices including road markings, highway signs, and traffic signals.

## Slide 10: Engineering Policy Guidelines
Standards for MoDOT Work Zones
  Reference Guide to MoDOT Operations
  Reference for Temporary Traffic Control
Article 600 Incidental Construction
  616 Temporary Traffic Control
    616.23 Traffic Control for Field Operations
http://EPG.modot.org
Notes: Explain
What the EPG is and how it can help research and find answers from common everyday scenarios to complex situations.
The EPG is a complete manual that covers all MoDOT operations from Right of Way, Design, Bridge, Construction, Traffic and Maintenance.
The EPG also includes documents in pdf format for printing in the field.
Article 616 covers Temporary Traffic Control
Subarticle 23 (616.23) is the Traffic Control for Field Operations manual (TCFO)
The typical applications can be found at the end of the TCFO and also at the top page in pdf format for viewing and printing.
If you have an internet connection, take time to show the class how to navigate to the EPG and to temporary traffic control as well as the TCFO.
(The picture of the EPG on this slide is a hyperlink to the EPG)

## Slide 11: Project Design and Construction Documents
EPG
Construction manual
Standard plans
Standard specifications
Job special provisions
TCFO
MUTCD
Notes: Other related documents to work zone planning.

## Slide 12
Core Work Zone Components

## Slide 13: Why is consistency important?
  Better recognition and understanding of the work zone
  Consistent interpretation
    Motorist know what is expected
  More rapid motorist response
    Controlled traffic flow
  Motorist respect
    Customer satisfaction rating will increase
  Reduced traffic control cost
    Safe work zones =less work zone accidents
  Reduces potential liabilities associated
  with work zones
Notes: When work zones are consistent the traveling public have a better understanding of what to expect while traveling through the state of Missouri. This will lead to less anxiety for the motorist, fewer incidents and overall safer work environment.

## Slide 14: Tort and Liability What is it?
Tort
  Provides the rights to compensation when another person harms their legally protected interests.
Negligence
  An act or omission within the scope of the duties of an individual, agency, or organization that leads to the harm of a person or public
Liability
  A situation in which a person is responsible to pay compensation for any damage incurred
Notes: Talk about what can we do to protect ourselves and workers.

## Slide 15: Liability in Work Zones
Inadequate warning
Malfunctioning devices
Work Vehicles
What Can We Do?
Notes: These are the top three reasons for torts in work zones.
Typicals include:
Traffic Control Devices/Signing: Traffic control devices are used at locations that typically involve higher levels of traffic conflict, and thus, many accidents happen near traffic control device locations. Most lawsuits against MoDOT involving traffic control devices usually involve malfunctioning devices (lights out/sign down) or an inadequate warning (device could not be seen from a far enough distance and no warning was given). Under the sovereign immunity waiver, MoDOT must correct hazardous conditions within a reasonable time once we are put on notice, and thus, downed signs and malfunctioning traffic lights need to be addressed as quickly as possible. –And we have systems in place to allow for that level of response.
Work Zones: Accidents increase in work zones. This increase in accidents occurs for several reasons. Work zones often do not follow the design consistency of the road and have signing different from regular articles of the roadway. These differences conflict with driver expectancy. This means, it can be very easy for a potential Plaintiff to make a claim that MoDOT is partially responsible for causing an accident that occurred in a work zone. However, it is important to remember that while work zones may conflict with a drivers’ expectations, they do not render a driver incapable of safely operating his/her vehicle. Proper safeguards and adequate warnings can be used to put drivers in a position to make good decisions. Proper safeguards and adequate warnings can be determined by referencing MoDOT’s standards, and although adherence to these standards will not guarantee complete safety in a work zone, it does mitigate the hazards to a great extent. In addition, consistently adhering to these standards allows MoDOT to later clearly explain its reasoning and it actions regarding the safety measures taken in any work zone, and in the event of a lawsuit resulting from an accident, this information can be used to show that a driver was in the position to make good decisions but failed to do so.
Fleet Vehicle Liability: MoDOT can be named as a Defendant in a lawsuit under a claim that one of our employees caused an accident while driving a vehicle as part of his/her work-related duties.

## Slide 16: Minimizing Liability
Document your duties and responsibilities
Follow “Standards of Care”
  National/agency standards and guidelines
    MUTCD, MoDOT Specs.
  Traffic Control Plan
  Document any deviations from
  the standards
Notes: It is important to “create a paper trail” for documentation purposes. Use the RBAs and TAs to talk through any possible situations that may occur.

## Slide 17: Minimizing Liability Cont.
Minimize project duration
Search for deficiencies
  If you find problems, FIX THEM
Keep workers trained and up-to-date
  Document training history
Share concerns with supervisors, managers
  Document conversations

## Slide 18: Minimizing Liability Con’t.
Safety 1st …ALWAYS
DOCUMENTATION
  Photos
  Video
  Drawings
  Inspections/Checklists
Notes: Best Practices:
take pictures or video (must comply with MoDOT personnel policy when doing this)
print out the TA beforehand every time to document location of signs and other pieces of equipment, etc.
document deviations to the setup (on printed TA)
document any changes

## Slide 19: Documenting a Work Zone Incident
Things to remember:
Memory is best directly after an event occurs
  Make your notes immediately, before you forget key details
Importance of Documentation
  Memories fade and people change jobs
What to document
  5 W’s: who, what, where, when, why
  Report only the facts
Meet with your regional counsel about any concerns
Notes: Remember to take notes before you forget key details, memory is best directly after an event occurs.
The documentation you create could potentially be the only information the department obtains about an incident, work zone set up, weather, and other significant details.
Written reports should include the 5 W’s - who, what, where, when, and why AND facts only, no opinions or conclusions to what might have happened.
If the incident is serious, you have concerns about the work zone or need more information – meet with your regional counsel to discuss further

## Slide 20: Review
What are the goals of the work zone?
  Zero work zone fatalities C. Traffic delays of 15 minutes or less
  Reduce all work zone crashes D. All of the above
The ________________ provides national standards governing all traffic control devices.
  EPG C. FHWA
  MUTCD D. MoDOT
What article in the EPG covers Traffic Control for Field Operations?
  610 C. 616
  612 D. 614
____________________ is an important part of minimizing liability?
  Documentation C. Liability
  Tort D. Memory
When documenting a work zone, employees should
  Make notes immediately D. Use the 5 W’s
  Have written documentation E. All of the above
  Report only the facts

## Slide 21
Section 2: Planning the Work Zone

## Slide 22: Where will you be working?
Where is the work going to occur:
Beyond shoulder (Mowing)
On shoulder (Edge Rut Repair)
Within the traveled way (Pavement Repair)
Notes: Explain and draw examples of typical encroachment
  Beyond shoulder w/ minor encroachment
  On shoulder w/ minor encroachment
  Within the traveled way…

## Slide 23: What type of work zone is needed?
Long-Term Stationary
Intermediate-Term Stationary
Short-Term Stationary
Short Duration
Mobile
Emergency
616.7.2

## Slide 24
Long-Term Stationary
Planned work
Occupy location more than 3 days
Shall use retroreflective and/or illuminated devices
Remove inappropriate markings
  Replace with temporary markings
Generally, the following devices are used:
  Post-mounted signs
  Larger channelizers and barricades
  Temporary traffic barriers
  Temporary pavement markings
  Work lighting
  Area lighting
  Warning lighting
  Temporary traffic signals

## Slide 25: Intermediate-Term Stationary
Planned work
Occupy location more than 1 daylight period
Occupy location up to 3 days
Planned nighttime work lasting more than 30 minutes
Retroreflective and/or illuminated devices shall be used
Consider the following if practical:
Altered pavement markings
Temporary traffic barriers
Temporary roadways
Post-mounted signs

## Slide 26: Short-Term Stationary
Planned daytime work
Occupying site for more than 30 minutes
Occupying site for less than 12 hours
Most maintenance and utility operations
  Workers and equipment move along the road without stopping, usually at low speeds
Generally, the following devices are used:
  Portable signs
  Flashing arrow panels
  Channelizers
  Fleet lighting
  Protective vehicles
  Truck-mounted attenuators

## Slide 27: Short Duration
Planned work
Daytime or nighttime
Occupying site up to 30 minutes
High-intensity rotating, flashing, oscillating or strobe lights may be used in place of signs and channelizing devices – should be augmented with signs and arrow boards
  Safety should not be compromised by using fewer devices because the operation will frequently change locations
Flaggers may be used for operations that involve frequent short stops on two-lane roads
Common Operations include:
  Litter cleanup
  Isolated pothole patching
  Isolated crack sealing
  Utility operations
  Signal Repair
Notes: For short duration, TA 17 & TA 35 can be used but employees should review other TAs to make sure the appropriate one is being used for the work that is being done.

## Slide 28: Mobile
Planned work
  Striping, sweeping, mowing, etc.
Moving continuously or intermittently
  Workers rarely exit vehicles during operation, such as retrieving large debris during sweeping, quick adjustment while striping, etc.
High-intensity rotating, flashing, oscillating or strobe lights may be used in place of signs and channelizing devices – should be augmented with signs and arrow boards
  Safety should not be compromised by using fewer devices because the operation will frequently change locations
Notes: Mobile operations would follow TA 17 & TA 35

## Slide 29: Mobile Con’t.
The use of Protective vehicles and/or TMAs should be determined by the appropriate TA for the operation and type of facility the work is being performed on
Consider scheduling during off-peak hours – especially under high-volume conditions
Mobile signs or stationary signing that is periodically retrieved and repositioned in the advance warning area may be used.

## Slide 30: Emergency
Unplanned work
Initial response
Repair/removal of safety concern including priority 1 items
  Refer to MoDOT’s Incident Response Plan (IRP)
Short-duration guidelines and appropriate TAs should be followed

## Slide 31: Performing Asphalt Pavement Improvement Operations
Asphalt Pavement Repair/Patching/Pavement Preventive Maintenance
Determine the work zone duration based on the maintenance activity or contracted project
  Long-term stationary
  Intermediate-term stationary
  Short-term stationary
  Mobile operation
  Emergency operation;
Apply the appropriate TA to meet the need
Plan the activity at least 14 days prior to the event
Input into the traveler information map

## Slide 32: Performing Asphalt Pavement Improvement Operations Con’t.
Coordinate maintenance and construction work to take advantage of lane/road closure(s)
Mid-late summer look at high-risk areas for asphalt pavement issues and repair before winter
    (job order contract (JOC), contractor, in-house)
For operations that require an emergency response (respond now instead of planned) - a request will be made for law enforcement or MoDOT Emergency Response (motorist assist) to go out with us during asphalt pavement improvement operations within ½ mile of an interchange
    If LE or ER are unavailable, work may continue
Notes: Use JOCs to address longitudinal joints prior to December or during winter months as material supplies allow
Districts should appropriately plan the use of law enforcement for contracts and maintenance work so funds can be dedicated/set aside

## Slide 33: Maximum Work Zone Lengths
What size of work zone is needed?
Length of work zones
Urban = 1 mile
Rural Divided = 2 miles
  Expressways/freeways
Rural Undivided = 3 miles
Notes: Ask: Participants to give examples of each definition. This will help you check their understanding of the material.
Explain
Work duration is a major factor in determining the number and types of devices used in temporary traffic control zones. The duration of a temporary traffic control zone is defined relative to the length of time an operation occupies a location. There are six categories of work duration - long-term stationary, intermediate-term stationary, short-term stationary, short duration, mobile and emergency
The work zone length could be modified for the urban or rural divided, at the discretion of the Pavement Specialist or Resident Engineer. Any changes must be document as to why.

## Slide 34: Will there be encroachments?
A significant encroachment means 10-feet of driving surface cannot be maintained for traffic
If encroachment exceeds the 10-foot minimum driving surface, the lane must be closed
Applied to shoulder or driving lane
Example: 2’ encroachment.
A 12’ lane leaving 10’ of driving
surface “lateral buffer”.
Notes: If an encroachments is necessary, it must be “MINOR” and short duration! Significant encroachments allows 10 feet of hard driving available for motorist to drive on. If a major encroachment occurs, (less than 10’ of hard driving surface) then the lane shall be closed. This would apply to either shoulder work or work in the lane. Document as to why encroachment was used.

## Slide 35: Hourly Volume Restriction
Interstates and Freeways
  Multi-Lane
  Two Lane
Type
  Urban
  Rural Divided
  Rural Undivided
High Volume
Low Volume
616.25 MoDOT Work Zone Guidelines – Roadway Capacities
Notes: In planning work on highways, it’s important to consider traffic volume. Traffic volumes help determine time of work with minimum disruption to traffic and allows you to gage the measures necessary to inform the traveling public or mitigate traffic backups when that work can’t be done in those specific time frames.
The number of vehicles moving through a work zone with a dropped lane reduces significantly. For more information view the Roadway Capacities chart in the EPG.

## Slide 36: Traffic Capacity
Capacities are estimated and may be adjusted for site conditions
Some examples include:
  Past experiences
  Lane widths
  Truck volume
  Geometrics
  Lane usage

## Slide 37: Major vs. Minor Highways
Major Highway – Functionally classified as principal arterials (this includes interstate, freeways and expressways)
  5,402 centerline miles
  17% of total state highway miles
  76% of total vehicle miles traveled
Minor Highway – Classified as minor arterials, collectors or outer roads (this includes lettered routes and referenced as farm to market roads)
  27,000 centerline miles
  83% of total state highway miles
  24% of total vehicles miles traveled
Notes: Reference
Major route system map
EPG (Better roads brighter future)
District (specific information)

## Slide 38: Major Highway Map
Major highway map may be found in the Engineering Policy Guide within the Better Roads Brighter Future.
EPG BRBF
Notes: Reference
Major route system map
EPG (Better roads brighter future)
District (specific)

## Slide 39: Developing a Transportation Management Plan (TMP)
Consist of strategies to manage the work zone impacts of a project
A TMP needs to be developed for all MoDOT projects/operations
Two Types
  Significant
  Non-Significant
Notes: The Transportation Management Plan (TMP) consists of strategies to manage the work zone impacts of a project.
The TMP may consist of only a Traffic Control Plan (TCP) for non-significant projects.
Projects that have been determined to have a significant impact on roadway users include, in addition to a TCP, both Transportation Operations (TO) and Public Information (PI) components. Refer to 616.14.8 for a discussion of significant projects.

## Slide 40: Developing a Transportation Management Plan (TMP)
Non-Significant
May only consist of a Traffic Control Plan (TCP)
Significant
Projects will be considered significant by meeting one of the following criteria:
  Interstate project occupying a location for more than 3 days with intermittent or continuous lane closures
  Project is on a major route in an urban area
  Project will cause capacity values to exceed those in the Work Zone Guidelines
    Typically:
      Not mobile operations
      State route traffic is not affected during construction
Should include Traffic Control Plan (TCP), Transportation Operations (TO), and Public Information (PI) components

## Slide 41: Develop a Traffic Control Plan (TCP)
Describes measures to be used to facilitate road users through a work zone or incident area
Shall:
Be consistent with MoDOT policy, guidelines, and standards
Meet the minimum requirements of the MUTCD
Maintain existing safety hardware
616.1
Notes: A TCP describes measures to be used for facilitating road users through a work zone or an incident area. The TCP should be consistent with MoDOT policies, guidelines and standards, and at minimum shall meet the provisions of Part 6 of the Manual on Uniform Traffic Control Devices (MUTCD). The TPC will maintain pre-existing roadside safety (hardware, object protection, slopes, etc.) at an equivalent or better level after project completion.
This is the simplest of maintenance operations, every work zone should have a TCP.

## Slide 42: Using the Engineering Policy Guide
Standards for MoDOT Work Zones
  Reference Guide to MoDOT Operations
  Reference for Temporary Traffic Control
  Article 600 Incidental Construction
    616 Temporary Traffic Control
      616.23 Temporary Traffic Control for Field Operations (TCFO)
http://EPG.modot.org
Notes: Explain
What the EPG is and how it can help research and find answers from common everyday scenarios to complex situations.
The EPG is a complete manual that covers all of MoDOT operations from Right of Way, Design, Bridge, Construction, Traffic and Maintenance.
The EPG also includes documents in pdf format for printing in the field.
Article 616 covers Temporary Traffic Control
Subarticle 23 (616.23) is the Traffic Control for Field Operations manual (TCFO)
The typical applications can be found at the end of the TCFO and also at the top page in pdf format for viewing and printing.
If you have an internet connection, take time to show the class how to navigate to the EPG and to temporary traffic control as well as the TCFO.
(The picture of the EPG on this slide is a hyperlink to the EPG)

## Slide 43: Navigating the EPG

## Slide 44: Navigating the EPG Con’t.

## Slide 45: Navigating the EPG Con’t.

## Slide 46: Navigating the EPG Con’t.

## Slide 47
Detail of project’s traffic control
  Simple reference manual (MoDOT EPG, MUTCD)
  Complex
  Know Key Terms
    May – Permitted
    Should – Strongly Recommended
    Shall – Mandatory
May be adjusted for field conditions
Select the Appropriate Typical Application(s) (TA)
Notes: It is the WZS’ responsibility to interpret the TCP and implement it in the field, in the safest possible manner.
A TCP may not take into consideration field conditions such as sight distance, curves, hills etc., it is the responsibility of the WZS to adjust the TCP based on field conditions
Diagrams are Linked to MoDOT’s EPG
Click on the drawings to show more detail if needed.

## Slide 48: Locating TAs in MMS

## Slide 49: Locating TAs in MMS

## Slide 50: Locating TAs in MMS

## Slide 51: Transportation Operations (TO)
Identifies strategies that will be used to mitigate impacts of the work zone on the operation and management of the area affected.
May include:
Demand management
Corridor/network management
Safety management and enforcement
Work zone traffic management

## Slide 52: Transportation Operations
Some examples include:
Capacity
Detours
Ingress/egress
Emergency services
Traffic generators
Law enforcement
Motorist assist
The TO should be developed and implemented in consultation with all stakeholders. (transportation agencies, railroads, public transit, law enforcement, emergency services, schools, etc.)
Notes: The TO is a part of the TMP.

## Slide 53: Public Information (PI)
Information may include:
Project characteristics
Expected impacts
Closure details
Commuter alternatives
Other traveler information strategies
Methods may include:
Direct mailings
Radio
Website
Public discussions
News releases
Portable Changeable Message Sign (PCMS)
Social media
Notes: Explain: Different types of communication that is used to deliver work zone information.
Note: Explain what actions are taken to get work zone information to your district community relations division and who within the district is to be contacted.
Also explain the amount of time ahead of the project that this information is to be submitted prior to the project or work zone. (most districts require a 2 week notice of intent to establish a work zone) Also note what is expected in reference to relaying emergency information for distribution to the public.

## Slide 54: Public Information
PI should be done by methods best suited for the project
Determined by utilizing the strategy matrix
PI seeks to inform the road user about the project, the expected work zone impacts, and any changing conditions
Notes: Explain: MoDOT provides general work zone information to the public through various outlets.
These include, among other things, publication of a statewide work zone map and work zone driving safety tips, posting of current work zone locations and conditions to the internet, promotion of Work Zone Safety Awareness Week, and advertisement of work zone safety-related messages via radio, television and billboards.
Note: Through these efforts, MoDOT positively influences work zone safety and mobility, as motorists gain access to information, they need to plan their trips and become more work zone conscious.

## Slide 55: Review
There are ______ types of work zones?
  6 C. 15
  3 D. 9
A long-term stationary work zone occupies the location for more than ________ days.
  5 C. 3
  1 D. 8
Intermediate-term stationary work zones occupy the location for how long?
  More than 3 days & up to 1 hour at night C. 6 hours
  More than 1 daylight period & up to 30 min. at night D. 12 hours
Short-term stationary work zone occupy the location for how long?
  1 day C. 6 days
  1 nighttime period D. less than 12 hours
A work zone occupying a site up to 30 minutes is considered?
  Short-duration C. mobile
  Emergency D. long-term

## Slide 56: Review Cont.
Mobile work zones move at speeds less than __________ mph?
  5 C. 15
  3 D. 10
Mobile operations follow TA#s _____ or _____.
  17, 35 C. 33,35
  10,18 D. 17,33
Emergency work zones are for repair/removal of __________________?
  channelizers C. debris
  TAs D. safety concerns
Planned maintenance operations should be planned at least ______ days in advance?
  1 C. 6
  14 D. 2
The maximum work zone length for a rural undivided roadway is ______________?
  3 miles C. 500 feet
  10 miles D. 1 mile

## Slide 57: Review Cont.
If encroachment occurs, at least ___________ of driving surface must be maintained?
  2 feet C. 10 feet
  5 inches D. 8 feet
Major highways include: (check all that apply)
  Interstates Expressways
  Farm to Market Roads Outer Roads
  Lettered Routes Freeways
Strategies to manage the impacts of a work zone project is called?
  Management C. Detour
  Transportation Management Plan (TMP) D. Safety
A significant TMP must meet at least 1 of 3 criteria. (check all that apply)
  Interstate occupying location more than 3 days with intermittent/continuous lane closures
  Typical Applications
  Major route in urban area
  Capacity values exceed those in the work zone guidelines
  Traffic Control Plan

## Slide 58: Review Cont.
Measures to be used for facilitating road users through a work zone or incident area.
  Channelizer C. Traffic Control Plan (TCP)
  Capacity D. Engineering Policy Guide (EPG)
The ________ is a complete manual that covers all of MoDOT operations including Right of Way, Design, Bridge, Construction, and Maintenance.
  EPG C. TO
  MUTCD D. FHWA
A _______________ details the project’s traffic control and may be adjusted for field conditions when necessary.
  channelizers C. debris
  Typical Application (TA) D. safety concerns
__________________ identify strategies that will be used to mitigate impacts of the work zone on the operation and management of the area affected?
  MUTCD C. Managers
  TCFO D. Transportation Operations (TO)

## Slide 59: Review Cont.
Some examples of transportation operations include: (check all that apply)
  Capacity Slide
  Detours Motorist Assist
  Crashworthy Traffic Generators
_________________ informs road users about a project, the expected work zone impacts, and any changing conditions.
  Public Information (PI) C. Social Media
  Transportation Operations D. E-Mail
Methods of public information include: (check all that apply)
  Word of Mouth Radio
  Direct Mailings Public Discussions
  News Releases Rumor
  Portable Changeable Message Signs (PCMS) Website

## Slide 60
Subsection 2A: Who will be driving through
your work zone?

## Slide 61: Self-Imposed Impaired Driving Abilities
Fatigue, sleepiness
Drive under influence
Distraction, cell phone
Notes: (Instructor is encouraged to elaborate on these topics, but they may be in the law enforcement, policies, ordinances rather than positive guidance.)

## Slide 63
Missouri Statistics

## Slide 64
Source: National Highway Traffic Safety Administration (NHTSA) Motor Vehicle Crash Data Querying and Reporting
Drivers Involved in Motor Vehicle Crashes
2019 FARS Annual Report File (ARF)
Missouri 2019 Driver Fatalities by Age
Notes: Instructor select to present whichever point she/he wants. However, showing this chart bring home the point that driver skills are different at different age group.
AGE
2019 Year
Driver Fatalities
15=< 5
16-19 37
20-24 56
25-29 60
30-34 50
35-39 36
40-44 42
45-49 50
50-54 50
55-59 60
60-64 32
65-69 38
70-74 13
75-79 16
80-84 22
85+ 18

## Slide 66: The Driving Task
The time to complete this process is called:
  Perception Reaction Time (PRT)
  Typical PRT is 2.5+ seconds
Perception
Identification
Decision-Making
Execution of the Decision
Driving Task Process
Notes: Based on my experience, that is what I think ahead of me. My job now is to identify exactly what it is and confirm it. After doing so, I must decide what to do—going straight, turn, change lane…. Then I must do this.
This process sometimes last for only a few seconds if not enough warning and guide signs post in advance to allow time in the identification and decision-making phase.
This process is called Perception—Response Time (PRT)

## Slide 67: Distance Traveled During PRT
Formula: d = (s * r) / 3.6
Notes: This table provides a sample of typical PRT values in seconds reported across a variety of studies.
speed = distance/time
Formula: d = (s * r) / 3.6
The AASHTO formula is as follows:
s = (0.278 * t * v) + v² / (254 * (f + G))
s is the stopping distance, measured in meters;
t is the perception-reaction time in seconds;
v is the speed of the car in km/h;
G is the grade (slope) of the road, expressed as a decimal. It is positive for an uphill grade and negative for a road going downhill;
f is the coefficient of friction between the tires and the road. It is typically assumed to be equal to 0.7 on a dry road and in the range from 0.3 to 0.4 on a wet road.

## Slide 68
Distance Traveled in 2.5 Seconds
Notes: Going 70 mph a driver can pass the length of a football field every 2.8 seconds

## Slide 69: Information Overload
Too much information on one sign
Multiple signs on one sign array
Too many signs in close-proximity
Complex roadway geometry
Work zone signs + regular signs
Notes: These are the most common situation for information overloading. Too much information on one sign makes the driver confused which information is needed. The driver simply doesn’t have enough time to read and digest the information presented. Similarly, multiple signs on one sign array confuses the driver of which signs has the appropriate information for the particular situation. Too many signs in close proximity poses similar problem. When the roadway geometry is complex, the driver need more time controlling the vehicle, steering, braking, pushing gas. So, the drive has little time less to read process and digest signs. In this situation, the potential for information overloading increases. Too many unnecessary information posted at work zone also causes information overloading.

## Slide 70: Effective Traffic Control
Must be visible to user (location)
Must be readable at user speed (size and design)
Must convey a clear, simple message
Maximize Visibility

## Slide 71: Summary
Drivers come in all ages and with different abilities
“Communication System” (traffic control) must be effective for high percentage of users
Constant inspection of system for missing or damaged devices is important to ensure effective system

## Slide 72
Section 2B: Work Zone Considerations
Providing drivers with the right information at the right time.

## Slide 73: Basic Considerations
Protected vs. unprotected area
Posted speed limit
Location of workers, equipment, and materials
Type of highway
Roadway characteristics
Type of operation

## Slide 74: Topics of Discussion
Pedestrian Considerations
Do you need to reduce the speed limit?
Do you need to request Law Enforcement?
What additional items do you need to remain safe in the work zone?
When will the work take place?
  Day
  Night
Notes: Speed Limits
Say: MoDOT has the authority to lower speed limits in their work zones for safety purposes. Remember, motorists will only reduce their speed if they perceive a need to do so.
When reducing a speed limit:
It should be on a case-by-case method
No speed limit shall be reduced below 35 mph
State: the Second Bullet refers to “Dynamic Speed Reductions” this is a new practice, where the speed is reduced only in areas affected by the presence of work being actually performed.

## Slide 75: Pedestrian Facilities
Provide a clearly delineated and usable travel path including adequate pedestrian access and walkways
Where existing pedestrian routes are blocked or detoured, provide information about alternative routes
Pedestrian routes should not be moved for non-construction activities such as parking for vehicles or equipment
616.4.1
Notes: There are numerous items to consider when planning for pedestrians in work zones.
If the TTC zone affects an accessible and detectable pedestrian facility, the accessibility and detectability shall be maintained along the alternate pedestrian route.
If establishing or maintaining an alternate pedestrian route is not feasible during the project, an alternate means of providing for pedestrians may be used, such as adding free bus service around the project or assigning someone the responsibility to assist pedestrians with disabilities through the project limits.

## Slide 76: Pedestrian Facilities Con’t.
The following 3 items should be considered when planning for pedestrians in Temporary Traffic Control zones:
  Pedestrians should not be led into conflicts with equipment, vehicles or operations
  Pedestrians should not be led into conflicts with vehicles moving through or around the worksite
  Pedestrians should be provided with convenient and accessible path
  that replicates as nearly practical the most
  desirable characteristics of the existing path
Notes: Consideration should be made to separate pedestrian movements from both worksite activity and vehicular traffic.
Blocked routes, alternate crossings, and sign and signal information should be communicated to pedestrians with visual disabilities by providing devices such as audible information devices, accessible pedestrian signals, or barriers and channelizing devices that are detectable to the pedestrians traveling with the aid of a long cane or who have low vision.

## Slide 77: Warning Signs for Closures
Sign should be at beginning of block at accessible crossing point
Barrier does not provide adequate warning
616.8.29
Notes: Unless an acceptable route that does not involve crossing the roadway can be provided, pedestrians should be appropriately directed with advance signing that encourages them to cross to the opposite side of the roadway
In urban and suburban areas with high vehicular traffic volumes, these signs should be placed at intersections (rather than midblock locations) so that pedestrians are not confronted with midblock worksites that will induce them to attempt dodging the worksite or making a midblock crossing.

## Slide 78: Maintain a Clear Sidewalk
Temporary ramps and boardwalks ensure smooth continuous surfaces
Notes: Signs and other devices mounted lower than 7 ft. above the temporary pedestrian pathway should not project more than 4 in. into accessible pedestrian facilities.

## Slide 79: Maintain a Clear Sidewalk Con’t.
Pedestrian zones should not be blocked by materials or equipment.
Notes: This could cause rough or uneven terrain difficult for pedestrians with disabilities to easily maneuver through.

## Slide 80: Barriers
Barriers defining the alternate route should:
  Be 36-42” high and continuous within 6” of the ground
  Extend around perimeter of construction site or entire length of alternate route
Barriers should not:
  Create sight distance restrictions
  Be constructed of materials that would be hazardous if impacted by vehicles
Notes: Ballast for TTC devices should be kept to the minimum amount needed and should be mounted low to prevent penetration of the vehicle windshield.
TTC devices, jersey barriers, and wood or chain link fencing with a continuous detectable edging can satisfactorily delineate a pedestrian path.
If a temporary traffic barrier is used to shield pedestrians, it should be designed to accommodate site conditions.

## Slide 81: Pedestrian Barriers
When pedestrian and vehicle paths are rerouted closer together, consider using temporary traffic barrier to separate
  Short intermittent segments shall not be used
Ineffective barriers (plastic tape) around site does not provide detection.
Notes: Short intermittent segments of temporary traffic barrier nullify the containment and re-directive capabilities of the temporary traffic barrier, increase the potential for serious injury both to vehicle occupants and pedestrians, and encourage the presence of blunt, leading ends. Adjacent temporary traffic barrier segments shall be properly connected in order to provide the overall strength required for the temporary traffic barrier to perform properly.
Tape, rope, or plastic chain strung between devices are not detectable, do not comply with the design standards and should not be used as a control for pedestrian movements.
Not detectable with a cane until already in work zone, no continuous guidance at ground level (or anywhere), if shoreline along edge of building, may walk right into point of barricade. Good that they are lighted with flashing beacon for the visual impaired.

## Slide 82: Pedestrian Paths
Should be continuous, smooth, hard for the entire length of pedestrian facility and located out of hazardous areas
  No curbs/abrupt changes in terrain
  Meet ADA requirements (EPG 900.1.11)
Access to transit stops should be maintained
Consider
  Existing pathways
  Bypasses
  Detours
616.8.28
Notes: Existing pathways – pedestrians can be directed to alternate pathways already existing in the work zone. This may include sidewalks on the other side of the roadway
Bypasses – temporary bypass routes can be provided where unobstructed and non-hazardous space is available in the right of way. Bypasses may be established in parking lanes os grass buffers in the work zone.
Detours – pedestrians can be instructed to use an alternate route when it is not possible to use other existing pathways
Pedestrians are reluctant to retrace their steps to a prior intersection for a crossing or to add distance or out-of-the-way travel to a destination.
Additional guidance for pedestrian movement through work zones is in EPG 616.24 Traffic Control for Non-Motorized Traffic.
When it is not possible to maintain a minimum width of 60 in. throughout the entire length of the pedestrian pathway, a 60 in. x 60 in. passing space should be provided at least every 200 ft. to allow individuals in wheelchairs to pass.

## Slide 83
Notes: A Columbus Ohio pedestrian path around construction project. The top picture is an up-close view of the top of a continuously detectable edging used for a person’s back of the hand. Being plastic, the edge would not be rough as a concrete barrier or splinter of a wood barricade. On the bottom, a 2-inch detectable edge is for a person’s cane for the visually impaired.

## Slide 84
Notes: The below picture shows a temporary curb ramp. As you can see a ramp coming up to a level platform and then a smaller ramp to the curb.

## Slide 85: Pedestrian Paths Con’t.
Movement of work vehicles and equipment should be limited across pedestrian paths
  Should be controlled by flaggers, when necessary
Access to workspace by workers and equipment should be minimized to avoid unacceptable changes in grade and rough terrain
Provide audible information devices, accessible signals and barriers/channelizing devices detectable with long cane, for pedestrians with visual disabilities
Notes: Pedestrians will tend to avoid these areas by attempting non-intersection crossings where no curb ramps are available.
Because printed signs and surface delineation are not usable by pedestrians with visual disabilities, blocked routes, alternate crossings, and sign and signal information should be communicated to pedestrians with visual disabilities by providing audible information devices, accessible pedestrian signals, and barriers and channelizing devices that are detectable to pedestrians traveling with the aid of a long cane or who have low vision.
Audible information devices might not be needed if detectable channelizing devices make an alternate route of travel evident to pedestrians with visual disabilities.

## Slide 86: Reduced Speed Criteria
Speed limit ahead signs installed when:
  Reduced speed applies to entire work zone
  Reduced speed is 15 mph or greater
Additional Criteria
  Reduce speed in 2 stages for reductions greater than 20 mph
  Cover existing speed limit signs
  Install speed limit signs at end of reduced speed area unless speed limit is posted within ½ mile of reduced speed area
Drivers will reduce their speed only if they clearly perceive the need to do so
Notes: Should be avoided as much as practical.
Large reductions increase speed variances and potential for accidents.
Smaller reductions < 10 mph cause smaller variances and fewer accidents.

## Slide 87: Fine Sign Requirements
Fine signs may be used at the discretion of the supervisor if the following criteria have been met:
  Work duration longer than 4 hours
  Reduced speed limit in effect
  Normal posted speed greater than or equal to 60 mph
  Workers on roadway without barrier protection
Installation of fine signs, their location and requirements shall conform to the diagram listed in the EPG 616.12.3 Work Zone Speed Limit Figures

## Slide 88: Use of Law Enforcement
The need to use law enforcement will be identified in the planning stage but, needs to be re-evaluated continually throughout the project
  Districts should appropriately plan the use of law enforcement for contracts and maintenance work so funds can be dedicated/set aside
Typical situations within/near Work Zones:
Speed enforcement
Temporary flagging situations
Incident management (crash or Priority 1)
Complex setups
Changes in setups
Notes: Depends Upon:
Placement within the work zone
How violators are ticketed
Where violators are pulled over
Law enforcement officials and vehicles should be located as not to be a hazard to the traveling public, themselves, or the workers.

## Slide 89: Law Enforcement Project Selection
Factors to consider when evaluating the potential use of law enforcement include:
  Type of facility
  Speeds
  Traffic control
  Other

## Slide 90: Law Enforcement Project Selection
Use of LE, both active and passive, is an effective tool to ensure traffic complies with work zone requirements arising from certain construction projects/maintenance operations
The use of law enforcement will vary from project to project
Use of LE is a great tool to help provide advance warning of our work zones and any potential queue
Details should be included in the traffic control plan and discussed with LE before work begins
Additional information can be found in EPG 616.16
Notes:   Instructor – make note there is a handout for law enforcement agencies on do’s and don’ts on proper placement within work zones (image above)

## Slide 91: Emergency Response Operations
For operations that require an emergency response (respond now instead of planned) - a request will be made for Law Enforcement or MoDOT Emergency Response (motorist assist) to go out with us during asphalt pavement improvement operations within ½ mile of an interchange
  If Law Enforcement or Emergency Response are unavailable, work may continue.
Take your time when gathering tools and equipment and follow requirements for the operation being performed (don’t cut corners). Making sure we have the proper equipment and are performing the operation correctly is crucial to safety.
Notes: Requesting LE presence is expected for asphalt pavement improvement operations and recommended for all other mobile operations.

## Slide 92: Review
PRT stands for_________________________.
  Perception Reaction Time C. Perception Reaction Trust
  Physical Readiness Training D. Personal Rapid Transit
Typical PRT is _______________.
  5 seconds C. 5 minutes
  2.5 minutes D. 2.5 seconds
Pedestrian facilities should not lead pedestrians into ___________; and should provide a clear, convenient, ________________ path replicating the existing pathway.
  Light, accessible C. conflict, rough
  Conflict, accessible D. safety, kind
Barriers should not create _____________________.
  safety C. Replicating Paths
  Paths D. Sight Distance Restrictions
Pedestrian paths should meet ________ requirements.
  Sight C. ADA
  Barrier D. Traffic

## Slide 93: Review Cont.
Movement of work vehicles and equipment should be ____________ across pedestrian paths.
  Limited C. Trusted
  Frequent D. Smooth
Speed limit ahead signs should be installed when the speed reduced is ________ or greater.
  5 mph C. 10 mph
  2.5 miles D. 25 mph
Typical situations where law enforcement might be used within/near a work zone include: (check all that apply)
  Speed Enforcement Temporary Flagging Situations
  Pedestrian Paths Complex Setups

## Slide 94: Group Project Stage 1

## Slide 95
Section 2C: Night Work Considerations
Providing drivers with the right information at the right time

## Slide 96: Should work be done at night?
The decision to work at night should be based on several factors:
  Traffic characteristics
  Construction schedule
  Impact on communities and businesses
  Other miscellaneous items
Notes: Nighttime work zones are becoming more common. As a WZS, you may be involved with nighttime projects.

## Slide 97: Advantages & Disadvantages
Reduced congestion/ lower volumes
Less business activity
Allows for normal traffic patterns at day
Worker's exposure is lower
Increased production
Improved seasonal working conditions
Reduced visibility
Greater probability for fatigued and/or impaired drivers
Disturbing surrounding communities
Night speeds tend to be higher
Reduced construction periods

## Slide 98: Night Work Considerations
Apparel
Lighting
Traffic control

## Slide 99: Retro-Reflective Clothing
Requirements for all employees that work on or near the right of way
Refer to MoDOT’s Safety Policies, Rules & Regulations Employee Handbook
Daytime
  Class 2 safety vest or shirt
  Meets or exceeds ANSI / ISEA 107-2004
Nighttime
  ½ hour before sunset to ½ hour after sunrise
  Class 2 or class 3 top (class 3 required)
  Class E bottoms
  Meets or exceeds ANSI / ISEA 107-2004

## Slide 100: Night Work Traffic Control
Traffic control for night operations does not require special set-up but could use enhancements
  Dimming PCMS, arrow panels, and warning lights
  Tighter channelizer spacing
  Larger devices
  Conspicuity markings
  Longer transition areas
Notes: MoDOT does not have to do anything special because we already have larger devices, channelizers, and larger signs.

## Slide 101: Night Work Lighting
Enhances worker safety
Lights shall not:
  Cause glare for motorists
  Spill onto adjacent properties
  Create shadows within the workspace
  Become a safety concern
A minimum intensity of five-foot candles is recommended

## Slide 102: Area Lighting
Required at flagger stations and specific areas significant to traffic guidance
  Will help traffic see and identify the flagger
Minimum intensity of 5-foot candles
Typically, a single light on a portable lighting unit

## Slide 103: The Need to Reduce Glare
Glare reduces driver’s ability to see you
Can be uncomfortable or disabling for workers or motorists

## Slide 104: Factors Impacting Glare
Distance between the driver and lights
Height of lights
Where the lights are aimed

## Slide 105: Minimizing Glare
Properly aim and adjust work lights
Consider shielding lights if proper aiming is not feasible
Inspect lighting frequently
Notes: Lighting should be as uniform as possible

## Slide 106: Example
This diagram shows how to minimize glare for tower mounted angles.
Notes: Tasks requiring high levels of precision and extreme care can require an average horizontal luminance of 20 foot-candles. The mounting height and offset distances of a light tower play a critical role in affecting visual performance and discomfort glare. The mounting height should be coordinated with light source lumens. Luminaire beam axis crosses normal lines of sight between 45 and 90 degrees. The lighting source should have an angle of no more than 60 degrees.

## Slide 107: Review
Advantages of nighttime work zones include: (check all that apply)
  Less busy reduced visibility
  Increased production allows for normal traffic patterns during day
  Higher night speeds
Nighttime work requires class 3 apparel, or 2 and _____________ bottoms.
  Lighter C. Class E
  Class 2 D. Dark
MoDOT follows ANSI _________ standards for safety apparel.
  107-2012 C. 108-2004
  107-2004 D. 108-2000
Night work lighting should not:
  Be bright Cause glare to motorists
  Spill into adjacent properties Create shadows within the workspace
  Be bold Become a safety concern
A minimum intensity of _____________ candles is recommended.
  5-foot C. 10-foot
  15-inch D. 18-inch

## Slide 108
Section 3: Device Selection and Quality Requirements
Notes: Once a TMP has been developed you will now begin planning and executing the work zone.

## Slide 109: Current MASH & NCHRP 350 Crash Criteria for Temporary Traffic Control
After December 31, 2016
  Significant modifications of TTC devices will be crash tested under MASH
  Non-significant modifications of TTC devices may be evaluated using limited element analysis
After December 31, 2019
  TTC devices shall pass MASH criteria
  Pre-2019 testing TTC may be used throughout their normal service life

## Slide 110
Topic | NCHRP 350 | MASH
Small car test vehicle | 820C vehicle (1,800 lbs.) | 1100C vehicle (2,420 lbs.)
Small car impact angle | 20 degrees | 25 degrees
Light truck test vehicle | 2000P vehicle (4,400 lbs.) | 2270P vehicle (5,000 lbs.)
Gating terminals and crash cushion impact angle | 15 degrees | 5 degrees
Variable message signs and arrow board trailers | No mention | Added to TMA crash test matrix
Support structure and work zone traffic control device testing | Only small car tested | Small car and light truck tested
Windshield damage criteria | Subjective/Qualitative | Objective/Quantitative
Vehicle rebound in crash cushion tests | None | Required
Test Speed | 62.2 mph | 62.2 mph
MASH vs NCHRP 350 Test Level 3 Changes
Notes: MASH testing was implemented due to increase of the sizes of the vehicles (weight, height and width).

## Slide 111: Crash Modeling and Crash Testing
Notes: The attached videos show how crash testing facilities obtain information of actual crash testing and develop computerization models. The models help the crash testing facilities to develop best possibilities to help a product to pass actual crash testing, which in turns help save funds.

## Slide 112: MoDOT MASH Update
Both NCHRP 350 and MASH temporary traffic control (TTC) devices can still be used
MoDOT purchases MASH compliant products, if available
MoDOT will phase out NCHRP 350 TTC devices overtime, MoDOT MASH SMT team will provide the time period

## Slide 113: Traffic Control Devices
Portable sign
Directional indicator barricades
Type I, II, and III barricades
Notes: Article 2 includes devices that are not expected to produce significant vehicular velocity change but may otherwise be hazardous. Examples of items in this class are barricades, portable sign supports, intrusion alarms, and plastic drums, vertical panels, or cones with lights. Testing of devices in this article will be required. However, some devices may qualify for reduced testing requirements.

## Slide 114: Traffic Control Devices Con’t.
Trim-line (Primary Channelizer)
Cones (minor routes-daytime only)
Drum-like
Direction indicator barricades
Vertical panels
Tubular markers
Notes: Explain the design and the use of channelizing devices.
Type I and Type II barricades may be used by entities other than MoDOT or its contractors

## Slide 115: Traffic Control Devices Con’t.
TMA’s
Barriers (temporary and permanent)
Impact attenuators
Crashworthy end terminals
Breakaway sign supports
Notes: MASH TL-3 and NCHRP 350 TL-3 Category 3 Criteria: In the past under NCHRP 350, truck/trailer mounted attenuators, barriers (temporary and permanent), impact attenuators, crashworthy end terminals, and breakaway sign supports were considered Category 3 devices. Since December 31, 2019, MASH guidance has been implemented within MoDOT. Under MASH, temporary traffic control (TTC) devices do not fall under any category as they no longer exist like they did under NCHRP 350 categories 1, 2, 3, & 4. Under MASH guidance, MoDOT can continue to use or implement NCHRP 350 TTC devices for the service life as determined by manufacturer of the device or when a selected date is decided by MoDOT senior management team to use only MASH devices.
At this time, TTC device manufacturers are in the process of testing devices to meet MASH criteria, but MASH tested products are slowly coming available.
Maintenance: Central Office personnel are updating bid specifications for MoDOT to have the ability to purchase MASH compliant devices when available. Some devices purchased on a statewide bid may be under the NCHRP 350 criteria because there is no other MASH tested device available.
Construction: Contractors shall furnish FHWA acceptance letters for TTC devices either meeting NCHRP 350 or MASH criteria, for example, truck/trailer mounted attenuators, crashworthy end terminals, and breakaway sign supports.
Barriers, impact attenuators, and some sign support assemblies do not require NCHRP 350 TL-3 or MASH TL-3 FHWA acceptance letters, just certification that the materials were constructed and installed according to specifications and standard drawings. The structures have been tested through the years and have proved to be crashworthy.

## Slide 116: MASH Update
Heavier Devices
Over 100 lbs
Trailer Mounted Devices:
  Area lighting
  Arrow panels
  Temporary traffic signals
  PCMS
Notes: Heavier devices (over 100-lbs) and trailer-mounted devices (TMD) (area lighting, arrow panels, temporary traffic signals, changeable messages signs, etc.) are considered not crashworthy. AASHTO/FHWA has agreed to continue studying the use and crash history of these devices. Time is needed to conceive and evaluate alternative measures to make these devices crashworthy. Certification for crashworthiness is not required. If possible, the Heavier and TMD devices should be shielded. Proper location, delineation, and removal of the devices when not needed are critical.

## Slide 117: Supplemental Warning
Flags atop signs in advanced warning area
  Required for Truck Crossing and Flagger Ahead Symbol signs
  Required for Road/Bridge Work Ahead signs on short-duration operations (less than 30 minutes)
  Each sign requires 2 MoDOT-approved flags
  Flags are to be 18” X 18”
  Follow EPG 616.6.2.2
616.6.2.2
Notes: 616.23.2.5.1.1 Flags and Advance Warning Rail System
This policy is mandatory and applies to all highways maintained by MoDOT.
Signs shall be enhanced with flags and barricades as shown in EPG 616.6.2.2.
Use the two examples in your workbook with the class.
Supplemental warning should enhance your sign package and bring more attention to the situation.

## Slide 118: Enhanced Work Zone Signs
Advanced Warning Rail System
  Long term work zones (Exceeds 3 days)
  Road/Bridge Work Ahead – sign
  Road Closed Ahead - sign
  Skid mount
  Post driven (Dig Rite)
Refer to EPG for guidance
616.10 Standard Plan
EPG 616.6.2.2
Notes: 616.6.2.2 Flags and Advance Warning Rail System on Signs
This is for long-term stationary operations only and to follow the requirements of Standard Plan (Drawing) 616.10AL.
And sign and device legend for required conditions.
The “Advance Warning Rail System” (AWRS) consists of three barricade rails and is installed to enhance warning signs. AWRS shall be added to work zones deemed long-term stationary operations. The warning signs that are enhanced with AWRS are:
  1. “ROAD/BRIDGE WORK AHEAD” (WO20-1) signs.
  2. “ROAD CLOSED AHEAD” (WO20-3) signs.
The following are, but are not limited to, ways to install the AWRS:
  1. The three barricade rails may be attached to U-channel, wood or PSST posts, according to the minimum sign area (sign and rails) as located in Table B of Standard Plan 616.10.
  2. A crashworthy skid-mounted sign and rail assembly.
  3. The sign and three-rail system may be mounted as separate crashworthy devices. The rail system shall be located directly in front of the sign with 7 ft. to 10 ft. separating the two devices.

## Slide 119: Warning Lights
Warning lights shall be yellow
Shall have a minimum mounting height of 30 inches from the bottom of the lens to the road surface
Shall not obscure the face of sign
Shall be equal or less than 3.3 lbs., if over than 3.3 lbs. or are not crashworthy; the lights shall have the battery packs mounted on the ground no higher than 18”
Be either:
Type A – low intensity
Type B – high intensity
Type C – steady burn
Sequential Flashing Warning
EPG 616.6.83
Notes: Warning lights are an option available to increase the target value of other temporary traffic control devices. Typically, a single self-contained unit that emits a yellow light is used for this type of lighting. There are four types of warning lights: A, B, C, and Sequential Flashing Warning.
Warning lights shall be mounted at a minimum of 30 in., measured from the base of the host device to the bottom of the unit, exclusive of any housing. In addition, lights should be installed so they do not hinder the functionality of the device they supplement or become a hazard themselves.
Type A (Low Intensity Flashing)
  Visible for 3000’ “Clear Night”
  Used on drum like channelizer
  Not used in shifts, tapers or long runs; Not used for delineation
Type B (High Intensity Flashing)
  Visible for 1000’ “Sunny Day”
  Used on advanced warning signs
  Not used for delineation
Type C (Steady Burn)
  Used on drum like channelizers; Used for delineation; Used for shifts, tapers, or long runs
Sequential Flashing Warning
  Visible for 3000’ “Clear Night”
  Used on Directional Indicator Board, trim-line, and drum-like channelizers; Used in merge and shoulder tapers; Used for delineation

## Slide 120: Quality Requirements - Acceptable
Picture 1 is an example of a proper placement of a road work ahead sign
Picture 2 is an example of the proper FLAGGER sign in advance of the hill vs. after the hill.
Picture 3 In urban areas with barrier walls and narrow shoulders, a truncated sign may be used as shown.
EPG 616.6.2
Notes: The signs and flags in Pictures 1, 2 and 3 are considered in good quality.
For enhanced visibility, a cone may be placed next to a sign.
NOTE: TTCDs may be highly visible during the day but may not be at night due to inadequate retro-reflectivity. MoDOT and Contractor representatives should drive through the work zone at night to check nighttime visibility

## Slide 121: Unacceptable
Notes: The above signs (4, 5, 6 and 7) are in unacceptable condition. Dirty or damaged signs should be cleaned, repaired, or replaced before being installed. When cleaning, follow manufacturer’s recommendations, so that the daytime and nighttime visibility of the sign is not adversely impacted. The MEN WORKING sign (8) should be replaced with worker symbol sign or WORKERS sign (WO-21-1 or 1a) to meet current standards Picture 9 shows unacceptable flags. Deteriorated flags should be replaced

## Slide 122: Nighttime Visibility Quality Requirements
Notes: The signs on the left are examples of acceptable nighttime visibility and signs on the right are examples of unacceptable nighttime visibility. Proper storing, transporting and covering can lengthen the life of a sign.

## Slide 123: Sign Installation Methods
Guidance for sign Installation methods are detailed in standard plan 610.10 within the EPG article 616.6.3 “work zone signing applications”
  Post
  Type 1 Portable
  Type 2 Portable
  Barrier
  Vehicle
All portable sign support systems shall comply with crash test requirements of MASH or NCHRP 350, test level 3
Notes: At this time, MoDOT can still use both MASH and NCHRP 350 products. Damaged or past its life, the products cannot be repaired or updated and must be discarded and a MASH tested product must be purchased.

## Slide 124: Portable Signs / Type 1
Skid
Fold-up stand
Minimum height 7’
  Urban
  Rural Divided
Minimum height 5’
  Rural Un-Divided
Rigid sign substrate
Minimum lateral clearance 3’
Permitted only where post mounting is not feasible
Shall comply with MASH or NCHRP 350 Test level 3
Notes: At this time, MoDOT can still use both MASH and NCHRP 350 products. Damaged or past it’s life, the products cannot be repaired or updated and must be discarded and a MASH tested product must be purchased.

## Slide 125: Portable Signs / Type 2
Easel
Fold up stand
Self-driving post
Type III movable barricade
Skid
1’ mounting height minimum
Minimum lateral clearance 3’
Notes: Explain
Signs as in the picture on the slide are within policy, provided that the signs can be installed in a plumb condition and that the bottom of the sign is a minimum of 1’ high from the near edge of the pavement.
Signs of this type should not be installed in ditch lines where the sign will be lower than the roadway or leaning.
In this situation an alternative sign mount may need to be considered.
MoDOT does have a vendor that can supply a “self-driving” post for conditions noted above that is 350 compliant.
An approved clamp must be used to attach the sign to the self-driving post.

## Slide 126: Portable Signs / Type 2 Con’t.
Sign Substrate – flexible or rigid
Can be left in place up to three days
Regulatory signs – use post height requirements, may be left in place longer than 3 days
Signs mounted on type III barricades, gore exit, and sidewalk closures may be left in place more than 3 days
Notes: Explain
Signs as in the picture on the slide are within policy, provided that the signs can be installed in a plumb condition and that the bottom of the sign is a minimum of 1’ high from the near edge of the pavement.
Signs of this type should not be installed in ditch lines where the sign will be lower than the roadway or leaning.
In this situation an alternative sign mount may need to be considered.
MoDOT does have a vendor that can supply a “self-driving” post for conditions noted above that is 350 compliant.
An approved clamp must be used to attach the sign to the self-driving post.

## Slide 127: Portable Sign Ballasts
For portable signs, ballasting should be limited to one sandbag height on the sign legs as shown in Picture 1
The use of channelizer rings as shown in Pictures 2 and 3 are unacceptable as it may make the installation not crashworthy

## Slide 128: Skid Mounted Sign Ballasts
Ballasting should be limited to one sandbag height on the sign legs as shown in Pictures 4 and 5.
The crossbar (Picture 5) should be no higher than 12 in.
Notes: Picture 5 shows an acceptable use of ballasting for a skid mounted sign. The crossbar (Picture 5) should be no higher than 12 in. (one sandbag over the crossbar is acceptable).

## Slide 129: What's Wrong ?
Picture 6 - large mound of sandbags, which if hit could present a ramping situation for vehicles
Picture 7 - two sandbags on the crossbar which is unacceptable because of two different sign-posts and two sandbags on the cross rail
Picture 8 - concrete is being used to ballast the sign, which is unacceptable

## Slide 130: Post-Mounted Signs
Break away support
Left in place “long term” more than 3 days
Minimum height 7’
  Urban
  Rural Divided
Minimum height 5’
  Rural Un-Divided
Lateral Clearance
  2’ with curbed articles
  6’ without curbed articles
* Posts shall be free of any bracing and extend no further above the sign except as needed for warning light attachment. See standard plan 903.3 for post installation details.
Notes: Ask
Do we need to call dig-rite before installation? YES WE DO!
It will take allot of planning prior to a project to get large quantities of dig rite locations completed.
Ask
If it is an emergency doe we call dig-rite? YES WE DO!
Explain to dig-rite you have and emergency situation and they will expedite the location of utilities.
The mounting height of a temporary post mounted sign is the same height as any permanent mounted sign on the same type of roadway.
It is important to be aware of lateral clearances so that the sign does not protrude into the travel way.

## Slide 131: Sign Installation
Appropriate # of posts for corresponding sign area
Posts should be embedded a minimum of 3 feet
Splices positioned entirely below 18 inches
Signs should not be obscured

## Slide 132: Post Mounted Splice
Appropriate # of posts for corresponding sign area
Posts should be embedded a minimum of 3 feet
Splices positioned entirely below 18 inches
Notes: Standard Plan 903.03 provides guidance on splicing of U channel and perforated square steel tube posts
Splice lap is positioned entirely below or above 18 inches, not to exceed 60 inches.
Wood post should not be spliced.

## Slide 133: Vehicle Mounted Signs
Affixed to:
  Protective vehicle
  Pilot car
  Pavement marking vehicle
Minimum mounting height 48” from road surface.
Sign substrate
  Flexible
  Rigid

## Slide 134: Portable Changeable Message Sign (PCMS) Displays
Each phase should convey a brief single thought
3 Lines
8 Characters (per line)
Should be a maximum of 2 Phases
EPG 616.23.2.5.2
Notes: CMS Phases
Refer to Page 18 in your workbook
Stress each bullet point on the slide.
Say:
Messages should consist of a maximum of two phases.
Typically, these phases consist of three lines of eight characters.
Each phase should convey a single thought

## Slide 135: Dynamic Message Signs (DMS)
Provides flexibility to display a variety of messages
Messages should consist of no more than two phases
Phase should consist of no more than three lines of text
Message should be brief and contain three thoughts
  Problem or situation that the road user will encounter ahead
  Location of or distance to the problem or situation
  Recommended driver action

## Slide 136: PCMS/DMS Displays
Distance to end of work zone
Estimated travel times
5-minute intervals
Located in advance of any potential queue
May display meaningful messages when workers aren’t present
WORKZONE
NEXT
5 MILES
EXPECT DELAYS
WORKZONE
NEXT
5 MILES
8
MINUTES
TRAVEL

## Slide 137: Flashing Arrow Panel
Intended to provide additional warning and directional information to assist traffic movement
Truck or trailer-mounted
5 operating modes
Stationary or moving operations
7 ft. mounting height
3 ft. offset from the traveled way
Only used on multi-lane facilities
Shall not be active while the protective vehicle/TMA are traveling to a different staging area/desired lane/work location
  The term protective vehicle represents the use of the protective vehicle within operations
Additional units located downstream of the taper in channelized areas shall display the caution mode
EPG 616.6.61
Notes: Ask: What are the 5 operating modes: Sequential Arrow, Flashing Arrow, Flashing Double Arrow, Alternating Diamond Caution, and Flashing Caution (4 corner caution).
MoDOT has invested to update the mobile operations truck mounted flashing arrow panels to have 25 bulbs as located on the truck picture to allow moving sign displays (Sequential Arrow, Alternating Diamond Caution).
Double arrow modes are used for stationary or moving lane closures on multilane roads, where traffic may pass to one or both sides, respectively.
In stationary operations the panel should be placed on the shoulder at the start of the lane closure taper or, where space doesn’t allow, within the closed lane behind the taper.
In moving operations, the unit is placed within the closed lane.
The caution mode is used for shoulder work, blocking the shoulder, work within the lane where the lane is not closed, and lane closures on two-lane undivided highways.

## Slide 138: Flashing Arrow Panel Con’t.
Arrow boards shall meet the minimum size, legibility distance, number of elements and other specifications
  Type B – normally truck-mounted & appropriate for mobile operations
  Type C – normally trailer mounted & intended for traffic control projects
  Type D – intended for use on MoDOT Emergency Response vehicles for emergency use until standard temporary traffic control devices are available
Notes: Type B & C arrow boards shall have solid rectangular appearances. Type D boards shall conform to the shape of the arrow. All boards shall be finished in non-reflective black.
Vehicle-mounted arrow boards should be provided with remote controls.
Arrow board elements shall be capable of at least a 50 percent dimming from full brilliance and the dimmed mode shall be used for nighttime operation of arrow boards. Full brilliance should be used for daytime operation.

## Slide 139
Notes: Acceptable arrow-heads are either all bulbs through the line or the bulb next to the tip of the arrow is off as per MUTCD. The color presented by the elements shall be yellow.
Below are items that would make the FAP installation unacceptable:
•More than one lamp, of those to be energized, out in stem and one or more lamps out in the arrowhead(s) when in the arrow (single- or double-headed) and one or more lamps out when in the caution (four corners) modes.
•Not appropriately dimmed at night

## Slide 140: Unacceptable Arrow Panels & PCMS
Notes: Picture 1 shows the correct flashing arrow panel (FAP) display, all lights are working and have the proper intensity. Picture 2 shows one lamp out in the arrow-head which is unacceptable. Picture 3 shows a truck blocking a FAP which is unacceptable. Below are items that would make the FAP installation unacceptable.
More than one lamp, of those to be energized, out in stem and one or more lamps out in the arrow-head(s) when in the arrow (single- or double-headed) and one or more lamps out when in the caution (four corners) modes.
Not appropriately dimmed at night
Pictures 5, 6 and 7 are examples of CMS that are unacceptable due to the lights being either too dim or out, as they are not providing a clear and concise message to the traveling public.

## Slide 141: Barricades
Portable or fixed device with one to three rails
  Used to close, restrict, or delineate all/a portion of the right of way
  May be offset to facilitate movement into and out of the closed area
  1 barricade for every 8’ of roadway and shoulder surface
  6-inch-wide stripes on rails shall be alternating orange and white retroreflective sloping downward at 45-degree angle in the direction road users are to pass
  Rails shall be 8 to 12 inches wide
EPG 616.6.68
Notes: Explain
When to use a barricade and what type of barricade may be used.
MoDOT recommends use of type III barricades but does allow Type I for non-motorized traffic and emergency road closures on 2 lane un-divided highways.
Use the next 3 slides to explain proper application of barricades regarding direction of barricade stripes.

## Slide 142: Barricades Types
Type 1
  One rail
  Non-motorized traffic operations on all highways
  Emergency road closures “2-lane undivided”
  Minimum length shall be 24-inches
  Used alone or in groups to mark specific condition or in series for channelizing road users
Type 3
  Used on freeways, expressways, and other high-speed roadways
  Minimum length shall be 48-inches
  One Type 3 barricade shall be used to completely close each 8-ft. of pavement
      Paved shoulders shall be included in the area to be closed
      Refer to EPG for additional information and specs
616.6.68

## Slide 143: Temporary Traffic Barriers (TTB)
A physical device used to prevent vehicles from entering the work area or separate vehicles in temporary 2-lane, 2-way traffic on normally divided highways
  May be used in lieu or in addition to channelizers separating motorized traffic from the workspace, an unsafe condition, or non-motorized traffic
    NOT used to form tapers
Required
  Roadway excavation edge drop-offs
  Bridge rehabilitations with bridge rail replacement
  Full-depth repairs
  Transition areas
Consider
  Long-term stationary operations or bridge repair work
* Consult with appropriate engineering staff for design requirements prior to installation
617.1
Notes: The preferred installation method for temporary concrete traffic barrier is free-standing, which requires a minimum 2-ft [0.6 m] buffer area behind the barrier to allow for lateral deflection in both work areas and lane separation situations. When free-standing installations are used on bridge decks/pavement drop-off, a 4-ft. [1.2 m] buffer area will be required. Concrete traffic barrier may be placed 6 inches [150 mm] from the edge of bridge decks/pavement drop-off if tie-down straps are used, however, a 3 ft. [0.9 m] buffer area must be maintained. On bridge decks/pavement drop-off where lateral deflection cannot be tolerated, the bolt through deck/pavement detail will be used. A proper transition from free-standing barrier to barrier with anchor bolts shall be installed on bridge decks. The method of installation on bridge decks will be determined by Bridge and will be shown on the bridge plans. The above requirements shall be maintained when developing staging or phasing of work requiring temporary concrete traffic barrier. The lateral deflection limits should be identified on the plans. No design exceptions will be allowed.
Proper installation, placement and protection is the following: Placement along/parallel to the pavement marking/lane. A barrier taper of a minimum of 8:1 flare rate. A barrier wall end is considered a blunt which shall be protected by sand barrels or an impact attenuator. Make sure all equipment/vehicles are located behind the barrier notice the Porta-Potty on the lower left picture.

## Slide 144: Temporary Traffic Barriers Con’t.
Proper connections are essential to prevent separation of a TTB if hit by an errant vehicle
3-Loop Barriers
2-Loop Barriers
Notes: On most projects, MoDOT uses the 3-loop Type F barriers on projects to protect drop-off locations, bridge deck repair, separating traffic, etc. The 3-loop Type F barrier can be pinned to the concrete and asphalt surfaces. The pins can be installed through the design holes in the foot area of the barrier. Currently, the 3-loop Type F barrier system is being MASH crash tested, until the crash testing is completed the current 3-loop Type F barrier system will be used.
For all temporary traffic barriers (TTBs) types, proper connections are essential to prevent separations of the TTBs when hit by an errant vehicle. Installing two 3-loop Type F barriers, the connection rod can be used without bottom washer and retainer bolt and nut. The 3-loop connection provide adequate friction so the connection rod will not come out on impact.
In some areas of Missouri, contractors use the older NCHRP 350 2-loop barrier system. As show in the pictures, each side of the barrier has 2-loops instead of 3-loops and no hole locations for pinning into the pavement surface. Currently, MoDOT allows the use of the 2-loop barrier.
When installing two 2-loop barriers, the connection rod shall have a bottom washer and retainer bolt and nut.
The 2-loop and 3-loop Type F barriers can be used together, but the barriers shall be connected with a connection rod and a bottom washer/retainer bolt and nut.

## Slide 145: Barrier End Treatments
Barrier ends present a safety concern and should be treated in one of the following methods:
Barrier flare
Barrier height transition
Crash cushions
  Impact attenuators
  Proprietary
Notes: Barrier flare – the barrier run may be flared to the limits of the clear zone. Where the existing shoulder slope or median slope is too steep, temporary grading should be provided or other end treatments should be utilized. Roadside Design Guide contains recommended barrier placement in non-level medians. The guidelines also apply to the outside shoulders
Barrier Height transition – is designed to redirect traffic away from the blunt end of the barrier, they are installed on the exposed ends or the barrier where the posted speed or design speed is less than 35 mph.
Crash cushions – are designed to absorb the energy of an impacting vehicle and reduce the force on a passenger. Installed on the exposed ends where the posted speed or design speed is greater than 35 mph. They are required on the upstream end for divided facilities, and both ends for all two-way facilities.
Impact attenuators – a group of freestanding sand barrels. Each barrel is designed with a specific weight of sand to absorb the energy of an errant vehicle
Proprietary – units such as the Quadguard-CZ and the ADIEM II may be used when sufficient width is not available for sand barrels. They require a paved surface matching the horizontal and vertical slopes of the barrier and installed parallel to the direction of the traffic.
Are Porta Potties approved crash cushions ???

## Slide 146: Crash Cushion
Used to mitigate the effects of errant vehicles impacting fixed roadside obstacles
Standard plan 612.20 includes installation guidelines for sand filled crash cushions
  Speed limit
  Size
  Weight
  Spacing
EPG 612.2
SP 612.20
Notes: Follow standard plan when installing crash cushions (sand barrels)
Based on speed limit the plan will dictate number of rows, length of cushions as wells as weight of each barrel in its respected position along with spacing of the barrels from each other.
Each barrel is designed with a specific weight of sand to absorb the energy of an errant vehicle. The sand barrel array's "footprint" length and width and the number of barrels will change based upon the permanent posted speed limit of the roadway. For the correct setup and array of sand barrel impact attenuators, refer to the manufacturer’s recommendations.

## Slide 147: Review
After December 31, 2019, all TTC devices purchased shall pass __________ criteria.
  MASH C. NCHRP 350
  Safety D. ANSI
MoDOT can still currently use NCHRP 350 and MASH products.
  True False
Supplemental warning flags shall be used on what signs?
  Merge Right Flagger Ahead Symbol
  Truck Crossing Lane Ends
  Merge Left Road/Bridge Work Ahead
The advanced warning rail system (AWRS) shall only be used in a _____________________ work zone.
  Mobile C. Intermediate-term
  Long-term stationary D. Emergency

## Slide 148: Review Cont.
Portable signs/Type 1 signs have a minimum height of ________________.
  5 or 7-foot C. 10-inches
  12-inches D. 15-foot
Portable signs/Type 2 signs have a minimum height of ________________.
  7-foot C. 15-inches
  1-foot D. 3-foot
Ballasting should be limited to ___ sandbag height on the portable sign legs?
  2 C. 1
  4 D. 3
Post-mounted signs will be left in place for more than _____ days and embedded a minimum of _______ feet.
  3, 3 C. 3,1
  1,3 D. 2,3

## Slide 149: Review Cont.
Vehicle mounted signs have a minimum mounting height of ____________.
  15 inches C. 13 inches
  56 inches D. 48 inches
PCMS displays should be a maximum of _____ phases.
  3 C. 2
  4 D. 1
Flashing arrow panels are only used on multi-lane facilities?
  True
  False
Barricades have 1 to ______ rails.
  10 C. 3
  4 D. 6
What direction do the chevrons go on a barricade.
  Direction they are to pass C. Left
  Right D. Opposite direction they are to pass

## Slide 150: Group Project Stage 2

## Slide 151
Section 3A: Site Preparation &
Work Zone Set-Up

## Slide 152
Advanced Warning Area
Activity Area
Termination Area
Transition Area
Buffer Space
(Longitudinal)
Work-Space
Protective Vehicle
Roll Ahead Space
Buffer Space
(Lateral)
Traffic Space
Notes: There are 4 areas to a work zone
As you page forward each area name will appear.
Explain to the class each area briefly. More detail will be given later for each area during the class.
The slide will continue with the different spaces. Explain each space to the class and give a brief description.
Advance Warning Area
Transition Area
Activity Area (Buffer/work area)
Termination Area

## Slide 153: Work Zone Set-Up
Stationary
  Advance warning signs
  Shoulder taper
  Flashing arrow panel
  TMA
  Channelizing device, temporary barriers
  Lane taper
  Termination taper
Mobile
  Advance warning signs
  TMA(s)
    Ex. – protective vehicle/TMA #3, protective vehicle/TMA #2, protective vehicle/TMA #1
Notes: Before any new detour or temporary route is opened to traffic, all necessary signs shall be in place. Most TTC zones are divided into four areas: the advance warning area, the transition area, the activity area, and the termination area.

## Slide 154: Knowing The Work Site
Review the work site
  Identify visibility issues
  Identify sign placement
Communicate with the crew
  RBA

## Slide 155: Advanced Warning Area
Motorists are informed of the work zone
Information is offered by a single sign or a series of signs/devices
    The first attention
    The second detailed information
    The third specific information
  More signs/devices may be used if situation warrants (arrow boards and message boards)
Notes: As you explain signing in the advanced warning area page forward will show signs for dived highway.
The first sign in the advance warning area is designed to get the attention of the motorist. Some people like to reference them as “A” Series Signs
The second sign(s) give more detailed information for the motorists – such as Right Lane Closed Ahead/ Shoulder Closed Ahead, etc. Some people like to reference them as “B” Series Signs. Additional signs are added in this series. However, the “A” and “C” series signs cannot be deviated
The third/final sign gives the motorist specific information of what to do, i.e. – Merge/Right. Some people like to reference them as “C” Series Signs
Portable Changeable Message Boards and Flashing Arrow Panels may also be used for additional signing

## Slide 156: Sign Spacing
Sign spacing based on:
  Posted speed limit
  Type of highway
    Divided
    Undivided
Distances may be adjusted “nominally” by increasing it to accommodate:
  Visibility
  Field conditions

## Slide 157: Transition Area
The path through the work zone should be obvious
Advance area warns motorists
Transition area is where motorists move to a specific place
Moving traffic through a work zone requires the use of quality tapers

## Slide 158: Types of Tapers
Merging taper
Shifting taper
Shoulder taper
Downstream (Closing) taper
One-lane, two-way taper

## Slide 159: Merging Tapers
Requires longest distance
  Drivers required to merge into common road space
Should be long enough to enable merging drivers adequate advance warning and sufficient length to adjust speeds to merge into adjacent lane before downstream end of the transition
  Important to provide full-length tapers (T2) where practical
Used to close a lane or combine traffic lanes on multi-lane facilities
Notes: For long-term operations, lane line markings are removed through the merging taper and temporary edge lines are to be provided to guide drivers through the taper and work area.

## Slide 160: Shifting Tapers
Used when a lateral shift is needed
Should have length of approximately ½ (T2)
  REVERSE CURVE or REVERSE TURN signs along with any required advisory speed plaques shall be posted prior to shift when ½ shifting tapers are used
Notes: For long-term operations, conflicting pavement markings are removed, and temporary markings provided to guide drivers through the tapers and work area. For short-term operations where it is not practical to modify pavement markings, a device spacing of 10 ft. is used.

## Slide 161: Shoulder Tapers
If shoulder is used as travel lane, normal merging or shifting taper should be used
Shoulder width is a determining factor
Length of taper and spacing of devices directly correlates to the type of roadway and the posted speed limit
  Should have length of approximately T1
Notes: Explain: A shoulder taper is calculated by speed limit according to the taper spacing chart for a divided highway. However, a shoulder taper, if applicable, for an undivided highway is 35 feet.
Example of calculated shoulder if one desires. A 40-45 mph highway with a 6-foot shoulder has a calculated shoulder taper of 90 feet according to the chart. Because 6 feet is equal to 60% of a 10-foot shoulder width. Therefore, 60% of 150 feet equals 90 feet. (185’ Taper = 111’ shoulder for 6’ Width).
Note: If you do not want to calculate the distance for a shoulder less than 10 feet. Simply use the chart. This would increase the number of channelizing devices needed and increase your safety.

## Slide 162: Downstream (Closing) Taper
Useful in termination areas to provide visual cue that access is available back into original lane or path that was closed
Should have approximate length of 100 ft.
  Devices placed 20 ft. apart

## Slide 163: One-lane, Two-way Tapers
Used in advance of activity area that occupies part of a two-way roadway - portion of the road is used alternately by traffic in each direction
Traffic should be controlled by flagger, TTC signal or STOP/YIELD sign
100-foot length
  Channelizing devices with 20 ft. spacing
Notes: Ask: When is a one lane, two-way taper used?
Possible Responses: In flagger operations, on bridges, etc.
Answer: It is an undivided highway. It covers one lane but has traffic originally flowing in both directions.
Explain: The difference between one-lane, two taper versus the shoulder/lane taper. If an undivided highway has a gravel or paved shoulder that may be perceived by motorist as drivable the following applies. Shoulder taper is 35 feet with a lane taper of 100 feet.
A short taper having a length of 100 ft. with channelizing devices every 20 ft. should be used to guide traffic into the one-lane section and a downstream taper should be used to guide traffic back into the original lane. For long-term operations, centerline markings are removed, and temporary edge line markings provided to guide drivers through the tapers and the work area.

## Slide 164: Lane Tapers
Length of taper and spacing of devices directly correlates to the type of roadway and the posted speed limit.
Notes: Explain: A lane taper is calculated by speed limit according to the taper spacing chart for a divided highway. However, a lane taper for an undivided highway is 100 feet.
Note: You may also calculate a lane taper for less than 12 feet the using the same process as we discussed in shoulder tapers.
Explain: There are different types of lane tapers on multi-lane highways. Some cases may have the center lane closed while in other cases you may have the right or left lane closed. Refer to the Typical Applications in EPG 616.8 Typical Applications or EPG 616.23 Traffic Control for Field Operations Manual.
Draw: Examples on the flipchart if needed.

## Slide 165: Taper Length & Spacing
Notes: Use the chart to determine the appropriate shoulder or lane taper length. The maximum distance in feet between devices in a taper should not exceed the limits as shown in the chart.

## Slide 166: Activity Area
Work-Space
  Closed to road users
Traffic Space
Buffer Space
EPG 616.3.6
Notes: Say: The activity area is broken down into three parts:
1. Workspace – can be stationary or mobile and is designated for workers, equipment, material, and protective vehicles. This area is closed to road users.
2. Traffic space – important that drivers are clearly guided through this area. This is the portion of the highway which road users are routed through the activity area.
3. Buffer space – separates road user flow from workspace or unsafe area. Might provide some recovery space for an errant vehicle. You can have more than one buffer space in a work zone.
Explain: Each area and the purpose of each.

## Slide 167: Buffer Space
Longitudinal Buffer
Lateral Buffer
Provides protection for traffic and workers
Notes: Ask: Is a buffer space required in every work zone ?????????
Answer: No, they are optional but, it is best practice to utilize a buffer space whenever practical
Explain: There are two types of buffers and the purpose behind both. A buffer space is an areas of empty space designed to keep an errant vehicle from entering the workspace or causing injury to self.
Longitudinal Buffer – the area that is also known as the recovery area and, if used. (This is not a place for anyone to park). May be placed in advance of workspace.
Lateral Buffer – clearance from the side of the workspace/activity area to the traffic path.

## Slide 168: Termination Area
Downstream of the work area
Typically short (100’ per lane)
Used to allow traffic to clear the work area and return to normal traffic lanes
Notes: Say: An area where traffic is returned to its normal path is the termination area. Resume speed limit sign is in this area.
Ask: Is a termination taper required or optional?
Answer: optional
Ask: Do you feel that a termination tapers add value to the job that you normally would perform?
Possible Answers: Yes, no, some value, little value, etc.
Explain: An optional 100-foot downstream taper per lane gives motorists clear directions to move back into their normal, uninterrupted path for divided highway. It is required for one-lane, 2-way taper. It is not required for operations on divided highway. However, MoDOT encourages the use of a termination taper if possible. It is permissible to use a lane taper and not a shoulder in the downstream taper.

## Slide 169
Core Work Zone Components

## Slide 170: Review
What are the 4 main components of a work zone?
  Buffer Space Advanced Warning Area
  Transition Area Workspace
  Activity Area Termination Area
The _________________ informs motorists of the work zone.
  Buffer Space C. Termination Area
  Advanced Warning Area D. Transition Area
The _________________ is where motorists move to a specific place.
  Advanced Warning Area C. Transition Area
  Buffer Space D. Termination Area
A __________________ requires the longest distance and is used to close a lane or combine traffic lanes on multi-lane facilities.
  Transition Taper C. Downstream Taper
  Shifting Taper D. Merging Taper

## Slide 171: Review Cont.
When a lateral shift is needed, a ______________________ is used.
  Shifting Taper C. Termination Taper
  One-lane, Two-way Taper D. Merging Taper
Which taper is used on a two-way roadway where a portion of the roadway is used alternately by traffic in each direction?
  Shifting Taper C. Merging Taper
  Lane Taper D. One-lane, Two-way Taper
The _________________ includes the work, traffic, and buffer spaces.
  Transition Area C. Activity Area
  Buffer Space D. Advanced Warning Area
________________ provides protection for traffic and workers.
  Buffer Space C. Activity Area
  Barricades D. Signs
The _____________________ is downstream of the work area and is typically 100 ft.
  Transition Area C. Buffer Space
  Termination Area D. Merging Taper

## Slide 172
Section 3B: Protective Vehicle/TMA
(Truck or Trailer
Mounted
Attenuators)

## Slide 173
Notes: SHOW the Scorpion TMA video from the manufacturer. Explain the importance of proper TMA operation and PM to the lives of the operator and workers in the work zone.

## Slide 174: Truck/Trailer-Mounted Attenuators
Energy absorbing equipment
TMAs are generally attached to the rear of the trucks/protective vehicles
Notes: SAY: Truck-mounted attenuators (TMAs) are energy absorbing devices designed to protect and reduce the severity of injury to the motorist and the TMA operator in the even of impact. The TMA is generally attached to the rear of the truck's protective vehicle.
All employees that drive a vehicle equipped with a TMA must be trained in the proper methods of installation, transporting, setup, operations, and preventative maintenance of the unit. Prior to operating any equipment employees shall complete the appropriate required training. To ensure that an employee understands his/her responsibility, every operator must successfully demonstrate the proper methods of attaching a TMA to a truck and perform operational and preventative checks and maintenance on the unit.

## Slide 175: The Need For Training
Protective Vehicle/TMA Drivers
  Most important job on the crew
  Responsible for safety of traveling public as well as safety of the crew
Notes: SAY: As the driver of a Protective Vehicle truck-mounted attenuator vehicle, your job is one of the most important on the crew. You are responsible for making sure that all other employees are adequately protected from errant vehicles in or around a work zone. It is the goal of MoDOT to provide consistent use of Protective Vehicles/TMA’s statewide.
Truck-mounted attenuators are designed to safely absorb the energy of an errant vehicle that crashes into it. Your job is to make sure that you are in the proper location to protect the crew, to provide ample roll-ahead distance, and to provide adequate warning to your co-workers and traveling public, when possible.

## Slide 176: Protective Vehicle/TMA Application
Used to safeguard the work-space from errant vehicles
Should provide sufficient warning to approaching traffic and maximum protection to workers and equipment
The use of Protective Vehicles/TMAs will be discussed later in the course
Notes: SAY: A protective vehicle is defined as any vehicle, other than a farm type tractor, used to protect workers or work equipment from errant vehicles, the protective vehicle may be equipped with a TMA as noted in the following section. Farm type tractors are not allowed as protective vehicles because of their low gross weights and high center of gravity.
This means the protective vehicle should be positioned so that it is clearly visible to approaching traffic and minimizes any vehicular encroachment into the workspace.
The protective vehicle should maintain a minimum of 150-foot clear roll ahead distance between the vehicle and the workspace.

## Slide 177: Responsibilities And Qualifications Of A Protective Vehicle/TMA Driver
Trained in TMA operations and procedures
Be alert, aware, observant, and able to react to surrounding conditions
Familiar with the daily tasks
Protect crew members and traveling public
Regularly check mirrors and monitor traffic
Be the eyes and ears of the crew and be able to alert them
Activation of audible alert and emergency alert lights (if available)
Check all lights and warning systems before beginning work for the day
Notes: REVIEW slide covering the following points:
SAY: It is the responsibility of the Protective Vehicle/TMA driver to be alert at all times. Communicate with your crew leader if you become tired or are not as alert as you were when you started. Stay off your cell phone.

## Slide 178: Seat Belts
The seat belt should be properly adjusted and snug on the operator
If involved in a crash, the seat belt and seat belt system should be inspected by a mechanic
NO Cell Phone!
Notes: SAY: Whenever possible, TMA dump trucks should have a high back seat for the operator. Seat belt usage is mandatory in a MoDOT owned or leased vehicles. It is extremely important that the driver of a TMA not only wears his/her seat belt, but also must have it adjusted properly.
Properly adjusted seat belts may minimize or reduce injuries. A seat belt should be secured in the manufacturer’s locking device and should be snug across the chest, not under armpit. If the truck has been involved in a serious crash, the unit should be inspected by a mechanic. This inspection should include the seat belt system.

## Slide 179: Inside the Cab
All loose items in the cab need to be secured
  PPE, lunch box, etc.
Drivers should be familiar with location of all activation buttons in the event of a strike - know where all equipment is located
Notes: SAY: A clean truck is vital to the operator’s personal safety. The operator of the protective vehicle is responsible for making sure that the cab of the vehicle is cleaned before use. Removing all trash and debris and securing all loose items may help prevent injury to the operator in the case of a traffic crash. Remember all cargo (lunchbox, hard hat, etc.) needs to be secured.

## Slide 180: Checking Mirrors
Make sure mirrors are adjusted properly
Regularly check your mirrors for activity going on around you and behind you
Notes: SAY: Mirrors are vital to the safe and successful operation of a commercial vehicle since they allow the driver to see behind the vehicle. Scan your mirrors constantly or at least every 7 seconds.
Auxiliary or convex mirrors give a larger field of view; however, they may distort the driver’s perspective by making objects appear smaller and farther away than they actually are.

## Slide 181: Emergency Alert Lights (EALs) & Audible Alerts
Tools to improve work zone safety by reducing the chances of a TMA being struck by an errant motorist
If an approaching vehicle is observed driving in the occupied moving work zone lane, TMA driver should activate the EALs and audible alert system by pushing the switch for a short duration
Team members are empowered to activate EAL and audible alerts as they feel necessary
If multiple TMAs in one operation, the hot seat TMA should include EALs
Notes: Existing MASH TMAs will be retro-fitted, this is optional on 350s. All new TMAs will be equipped with audible alerts and EALs.
EALs and Audible Alerts are activated simultaneously when the vehicle is equipped with the devices.
It is not recommended to leave the lights on for long periods of time because long-term or continuous use may reduce the effectiveness of the EAL.
An advanced auto detection warning device is being developed for testing.

## Slide 182: Installation of EALs & Audible Alerts
MASH TMAs
  All new purchased MASH TMAs will be equipped with EALs and Audible Alerts
  Existing MASH TMAs will be retro-fitted to included EALs and audible alerts
NCHRP 350 TMAs
  At district’s discretion, existing NCHRP 350 TMAs may be retro-fitted to include EALs and audible alerts
Contractor TMAs
  EALs and audible alerts are optional for contractor TMAs

## Slide 183: Rotation of Drivers
Understanding human factors
Drivers should be rotated to reduce mental fatigue, daydreaming, and to increase driver attention
All of this helps reduce complacency
Rotation allows for other drivers to gain experience
Notes: SAY: When practical, drivers should be rotated throughout the day. Inattention, mental fatigue, and daydreaming may occur when a driver is in the TMA for long periods of time.
Supervisors need to be aware of these variables and rotate drivers when feasible to eliminate some of the human factors. Having fresh, attentive employees in the TMA truck during moving operations will maximize the driver’s safety as well as the employees working in or around the TMA truck.
CLICK and SAY: DO NOT use your cell phone while in the TMA. You need to stay focused.

## Slide 184: Visibility
Sight Distance Issues
  Pay attention to hills, curves, and other sight distance items that might be present
  Position protective vehicle with TMA before hills or curves
Decision Point Issues
  Pay attention to merging, diverging, and intersecting locations
  Queueing or stopped traffic
  Position protective vehicle with TMA where it is easily identifiable by all approaching traffic

## Slide 185: TMA Placement
If the Protective Vehicle/TMA #3 must occupy the driving surfaces, it is allowed to be in the lane if the work involved is less than 30-minutes and the work area is less than 1-mile and follows guidance in note F on the TA
If the time and distance cannot be met, the project shall have advanced warning
If roadways do not have enough shoulder for a Protective Vehicle/TMA #3 and enough shoulder for a sign/wall sign, a LEFT/CENTER/RIGHT LANE CLOSED AHEAD sign may be located on the left or right shoulder upstream of the mobile operation
If a Dynamic Message Sign (DMS) is located within 1/2 mile to the mobile operation, the TMC should provide information to DMS for the traveling public
Notes: Utilize the Highway Safety & Traffic Division as well as the Safety & Emergency Management Unit for guidance if something is unclear or you are uncertain about something on a TA.

## Slide 188: Work Near Multi-Lane Sections Near or Within Deceleration/Acceleration Ramps
If the area of work includes a deceleration ramp and/or acceleration ramp and the duration of work is for 10 minutes or more near that deceleration and/or acceleration ramp, a RIGHT LANE CLOSED AHEAD sign or Protective Vehicle/TMA should be located at the off-ramp shoulder or on-ramp gore point.
If a Dynamic Message Sign (DMS) is located within 1/2 mile to the mobile operation, the TMC should provide information to DMS for the traveling public.
If traveling public has an alternative/detour route, the on-ramp may be closed while the mobile operation is located close to the on-ramp.

## Slide 190: Responsibilities During Mobile Operations
Keep the vehicle in gear and the wheels following the centerline
Do Not Leave Your Lane of Traffic
  If you notice an errant vehicle coming towards your Protective Vehicle/TMA, DO NOT leave your lane of traffic. This would expose the crew to a crash and possible injury. If possible, you should try to alert the crew and proceed forward to lessen the impact.
Notes: SAY: During mobile operations, operate your Protective Vehicle equipped with a TMA as you would any other vehicle. Keep the vehicle in gear and the wheels following the centerline. Maintain your speed to provide a minimum roll-ahead space of 150 feet. Pay attention to hills, curves, or other sight distance items that might be present.
If you are operating a Protective Vehicle equipped with a TMA, your job is to protect the crew and yourself. If you notice an errant vehicle coming towards your Protective Vehicle equipped with a TMA, DOT NOT leave your lane of traffic. This would expose the crew to a crash and possible injury. If possible, you should try to alert the crew.

## Slide 191: Preventive Action During Mobile Operations
Preventive action may include moving the vehicle forward to lessen impact.
  If the operator takes preventive action, he/she should be observant of all crew workers and equipment including the next TMA, to maintain at least 150 feet roll-ahead distance.
  In instances where you do not have the recommended 150 feet roll-ahead distance, engage the parking brake and DO NOT roll forward to lessen the impact.
Protective Vehicle/TMA #1
  If any employees exit their vehicles in the work activity area, the TMA vehicle operator closest to work activity shall engage the parking brake.
Protective Vehicle/TMA #2
  If an operator feels he/she is about to be struck by an oncoming vehicle, the operators may take preventive action as to lessen the impact.
Notes: Employees should not exit TMAs that are in the driving lane during mobile operations unless an additional TMA is providing protection.

## Slide 192: Stationary Operations
Wheels of the Protective Vehicle/TMA should always be aligned with traffic.
Emergency brakes must be set, and the transmission put into neutral.
Once the Protective Vehicle/TMA is placed in position for the stationary operation, the driver should exit the vehicle and proceed to the work area.
The Protective Vehicle/TMA should not be occupied again until repositioning is necessary, or the work zone is being removed.
Notes: SAY: The wheels of the protective vehicle should be aligned with traffic at all times. In addition, the emergency brake shall be set and the transmission put into neutral.

## Slide 193: Things to Remember
Regularly check TAs for updated guidance (EPG 616.8)
Regularly check EPG for updated guidance (EPG 612)
All NEW TMA purchases must be MASH compliant

## Slide 194: Review
The job of a _______ is to safeguard the workspace from errant vehicles.
  Barricade C. Termination Taper
  TMA D. Mirror
Responsibilities and qualifications of a TMA driver include, but are not limited to: (check all that apply)
  Protect crew members and the public
  Check their cell phone
  Regularly check mirrors
  Activate audible alerts and emergency lights if necessary
  Assign crew member tasks
  Check all lights and warning systems before beginning work daily
Rotating TMA drivers helps reduce:
  Mental fatigue C. Daydreaming
  Complacency D. All the above

## Slide 195: Review
The TMA should never ________________________.
  Protect the crew C. Set the parking brake
  Be in neutral D. Leave their lane of traffic
A TMA should always leave at least 150 ft. of _______________ during mobile operations.
  Work Area C. Taper
  Roll ahead space D. Signs
During stationary operations, the wheels of the TMA should always be aligned with what?
  The center line C. Traffic
  The activity area D. All the above

## Slide 196
Section 4: Flagging Operations

## Slide 197
I’m Safe???
Your job is the most important
one on the crew!
Flaggers shall not sit in a chair
Flagger should be alone without distractions of other employees
Flag paddle shall not be unattended
Stop/slow paddle must remain visible to all traffic
Co-worker is not wearing high-vis apparel
Flagger shall remain off roadway until traffic is stopped
Notes: Instructor should ask the class to list in their work book, what they see wrong in this photo

## Slide 198: Qualifications of a Flagger
Ability to:
  Receive and communicate specific instructions clearly, firmly, and courteously
  Control signaling devices (such as paddles & flags) in order to provide clear and positive guidance to drivers approaching a TTC zone in frequently changing situations
  Ability to understand and apply safe traffic control practices, sometimes in stressful or emergency situations
  Ability to recognize dangerous traffic situations and warn workers in sufficient time to avoid injury.
EPG 616.5.1 Qualifications for Flaggers (MUTCD 6E.01)

## Slide 199
Mentally Alert
Not under influence of alcohol or drugs
Beware of the effects of:
  Prescription medication
  Over-the-Counter
Well rested, not drowsy
Flaggers Must Be
I – Illness
M – Medications
S – Stress
A – Attitude
F – Fatigue
E - Education
Notes: Instructor could possibly ask: What are some other things that can affect a person's mental alertness? Have a short discussion regarding the comments, possibly provide guidance as to what someone should do, if they are not mentally alert. Remind them to speak to their supervisor prior to going out on the road.

## Slide 200: Flaggers Must Be
In good physical condition
Good sight
Good hearing
Ability to move quickly
This is NOT an assignment for modified duty /injured workers
Notes: Instructor should explain what it means to be:
Good Physical Condition
Good Sight
Good Hearing
Able to move quickly and why?

## Slide 201: Flaggers Must Be
Professional, Authoritative & Courteous
Dress appropriately
Clean and Neat appearance
  Clean PPE
Polite when providing firm directions to the traveling public
  You must remain calm with irate motorists
Confident and competent
Notes: Instructor should explain what it means to be:
Professional
Authoritative
Courteous
  Give personal examples of each

## Slide 202: Flagger Guidelines
Before any flagging begins you should:
Select a qualified flagger that has been properly trained
Have proper safety attire and equipment
Select flagging method and location
Have all advance warning signs in place
Flagger station must be visible to motorists
  If possible, the crew and other flaggers
Notes: Before any flagging begins you should:
Select a qualified flagger (critical issue)
If someone is sick or having personal problems, do not let them flag
Flaggers need to be mentally alert and in good physical condition
Have proper attire and equipment
You shall have on an orange vest and hat. If there is a chance of falling objects, you will be required to wear an orange hard hat
Have a stop/slow paddle (acceptable condition) and 2-way radios (in working order-check batteries)
Work Zone Signing
Make certain that advanced warning signs are in place and correct
Only one sign can be used, it must be the flagger symbol sign (on cover of workbook)
This is a new universal sign because of different languages (as compared to “FLAGGER AHEAD”)
SAY: As a flagger, you are required to be clean, neat, and fully dressed at all times when on the job, either day or night. Be prepared for changing weather conditions by bringing suitable clothing and other necessary things such as sunscreen, insect repellant, and water. You are the first person the traveling public will encounter; sloppy dress or appearance will not be tolerated and will present a non-professional image. Remember you’re representing MoDOT.
REVIEW slide.
ASK: Who remembers from the Basic Safety class what specific type of PPE is required for flagging?
  Hi-vis hard hat.
    Daytime
    Class 2 safety vest or shirt
  ½ hour before sunset to ½ after sunrise
    Class 3 or class 2 top + class E pants

## Slide 203
Notes: Instructor should explain:
What PPE is required for daytime flagging operations
Stress the importance that the PPE should be clean and in good condition

## Slide 204
Notes: Instructor should explain:
What PPE is required for nighttime flagging operations
Stress the importance that the PPE should be clean and in good condition

## Slide 205
Where I Am Is Safe
What I Use is Safe

## Slide 206: Stop/Slow Paddle
Shall be retro-reflective
Shall be octagon shape on a rigid handle
  Preferred height of 5-7ft.
Shall be 18 inches with 6-inch letters
Shall be in quality condition
Use of flags should be limited to emergency situations only
Notes: Flaggers shall use a STOP/SLOW paddle, a flag, or an Automated Flagger Assistance Device (AFAD)
The use of hand movements alone shall be prohibited except for law enforcement personnel or emergency responders at incident scenes

## Slide 207: Factors you must consider:
Hills
Curves
Obstructions
Shade – hard to see people in shaded area
Glare – lighting devices or angle of sun
Color Contrast – wearing an orange vest standing next to a similarly colored truck
Bad Weather
Darkness
Factors that Affect Sight Distance
Notes: Instructor should explain:
The importance of maximizing your visibility based on location of work
The importance of adjusting to field conditions to ensure the flagger station is located properly

## Slide 208
Flagger Station
Flaggers should always be clearly visible to the first approaching road user
    500 ft. daytime/1,000 ft. nighttime
Flaggers should face oncoming traffic
Flaggers should also make themselves visible to other road users after first vehicle stops
Notes: To Increase Visibility:
Do Not Stand Like a Statue
Move/Raise/Lower the Stop/Slow Paddle
Move your Body with small side to side movements

## Slide 209
Flagger Station
Flagger stations shall be located such that approaching road users will have sufficient distance to stop at an intended stopping point
Notes: Instructor should explain:
The Stopping Sight Distance Chart shown on slide
Give examples and explain the need that a flagger station must be separated from the work area, crew and any/all equipment.

## Slide 210: Flagger Station
Flaggers should be stationed sufficiently in advance of the workers to warn them of approaching danger by out-of-control vehicles
Flagger stations should be located such that an errant vehicle has additional space to stop without entering the work-space
The flagger should identify an escape route that can be used to avoid being struck by an errant vehicle
Consider audible warning devices:
Horns
Whistles

## Slide 211: The flagger should stand alone, at least 100 ft. from: Other workers Work vehicles Equipment
Flagger Station
Flagger must identify an escape route
Notes: Flagger stations should be located such that an errant vehicle has additional space to stop without entering the workspace
The flagger should identify an escape route that can be used to avoid being struck by an errant vehicle

## Slide 212: Flagger Station
Flagger cannot be more than 1 mile away from the flagger symbol sign
Only 1 flagger symbol sign may be posted, per travel direction
Notes: Instructor should explain:
Why and the importance of only 1 flagger symbol sign may be posted per travel direction

## Slide 213: Nighttime Flagging
Nighttime hours:
Begin one-half hour before sunset
End one-half hour after sunrise
Notes: Except in emergency situations flagger stations shall be illuminated at night

## Slide 214: Nighttime Flagging
Flaggers shall be visible at a minimum distance of 1,000 feet
All signs shall be retro-reflective and channelizing devices shall have two retro-reflective bands
Glow wands or handheld lights are recommended
Notes: Instructor should explain:
Night Time Flagging Operations
The Challenges of flagging at night, give personal examples

## Slide 215: Glare
Lighting shall not produce a disabling glare to:
Traveling Public
  Traveling in either direction
Flaggers
Crew Workers
Factors impacting glare are:
Lighting unit set-up location
Height of lighting unit
Direction the light units are aimed
Notes: Instructor should:
Reinforce the requirement to have Area Lighting at the flagger station
Headlights on equipment is not considered to be a suitable light source
Explain the issues associated with glare

## Slide 216: Flagger Duration
Flaggers should not flag for more than two hours at one time
  Unless it is an emergency situation
Supervisors shall provide flaggers with a 15-minute break from flagging in non-emergency situations
In emergency situations, the supervisor should make every effort to rotate or relieve the flaggers with another qualified flagger every two hours
Notes: Review slide
Explain That this is in an ideal situation. It is just as much your responsibility to remind your crew leader it’s time to rotate or take break as it is there’s. Remember to be respectful.
REVIEW slide

## Slide 217: Flaggers Cannot Be Distracted:
Do Not Use:
Cell phones
Ear buds or headphones

## Slide 218
Flagging Hand Signals
&
3-2-1 Cone Procedure

## Slide 219
Use of Hand Signaling Devices by Flaggers (MUTCD 6E-3)
Notes: Instructor should:
Demonstrate the hand signals
  Reinforce the importance of giving firm, controlled and quality hand signals
Explain the need to keep the flag paddle in the right hand

## Slide 220: Step 1: Stopping Traffic
Stop/Slow Paddle is fully extended from the body
Left hand is up with open palm, in STOP position
Face Traffic, from the edge line/edge of pavement
  Ensure STOP sign is facing oncoming traffic
The following photos represents open lane of work zone. Flagger at opposite end controlling traffic of the closed lane (the lane work is actually taking place in) would not move the cone(s). Instead, you would motion traffic to drive around the cone(s).

## Slide 221: Step 2: Traffic is Stopped
Once traffic has stopped, move out towards the center of the lane
Keep the Stop/Slow Paddle in your right hand and position it out towards the center line, be sure not to cross the line with the Stop/Slow Paddle
Keep visual contact with drivers of stopped vehicles
Keep left hand raised with palm facing driver, signaling to stop, until traffic has stopped

## Slide 222: When you arrive at Center Line
You may put your left hand down once traffic has stopped
Continually monitor traffic flow, from the opposite lane along with the vehicle(s) you have stopped within your lane

## Slide 223: Step 3: Preparing to Release Traffic
Once you have confirmed opposing traffic is clear, make your way back to the shoulder taking the cone (as shown) with you
Be sure to keep STOP visible to the stopped traffic

## Slide 224: Step 4: Releasing Traffic
Once on the shoulder, rotate the Stop/Slow Paddle to SLOW and release traffic
Direct traffic by signaling with your arm and waving vehicles through

## Slide 225
3-2-1 Cone Procedure
Mobile & Short Duration Operations
When lane width is less than 12 foot, 2 cones is recommended during Short Duration and 1 cone must be used during Mobile Operations
Long, Intermediate and Short-Term Stationary Operations
When lane width is 12 foot, use of 3 cones is recommended
When lane width is less than 12 foot, 2 or 1 cone(s) may be used
Notes: These photos represent the open lane of the work zone. The flagger at the opposite end controlling traffic of the closed lane (the lane work is actually taking place in) would not move the cone(s). Instead, you would motion traffic to drive around the cone(s).
There may be instances when you have to move the cone to allow traffic to pass, such as when traffic has stopped too close to the cone or to accommodate a OWOD load. A minimum of 1 cone or trim-line channelizer must be used. Additional Channelizers may used at the discretion of the: District Maintenance Engineer, Safety & Health Manager, Superintendent and/or Supervisor.
Contact your Safety & Health Manager and/or Work Zone Coordinator with any questions

## Slide 226: Flagger Communication Rule
One flagger should be designated as the lead flagger
This person has control over all flagging operations and emergency vehicles right-of-way
Notes: REVIEW slide. SAY: If you hear or see an emergency vehicle, communicate with the lead flagger who will determine further actions.

## Slide 227: Emergency Vehicles
Have right of way priority in a work zone
  Only when it is safe to proceed
Notes: Instructor should ask: what do you do when emergency vehicles approach the work zone?

## Slide 228: How Do Flaggers Communicate to Each Other?
Two-way hand-held communications
Maintain a clear sight distance
Hand signals
Raising a stop/slow paddle
Notes: Maintain a clear sight distance Be able to clearly see the other flagger so you can determine what the other flagger is doing
Two-way hand held communications Designated for flagger communication Truck/car radios are not permitted unless it’s an emergency Ask students “What do you do if your hand held radio quits?”
Hand signals Ask students for more ways to communicate (tip hat, raise paddle, wave, OK sign, and thumbs up or down) Both flaggers need to understand all hand signals and know what they mean
Raising a paddle Demonstrate how to raise a paddle to release traffic

## Slide 229: Communication Devices
Preferred method of communication
Use when sight distance is a problem
Use whenever possible while flagging
Only use approved FCC devices
Ask yourself the following questions:
How many walkie-talkies do we need?
Do I need to take extra batteries?
Is the unit working and fully charged?
Be Professional; remember this is an open frequency

## Slide 230
Single Flagger
Operation
Notes: Instructor should explain the Single Flagger Operation and when it is acceptable to conduct Single Flagger Operations

## Slide 231
Two Flagger Operation
Notes: Instructor should explain the Two Flagger Operation

## Slide 232: Advance/Additional Flaggers
Use when sight distance is limited
Side roads and parking lot entrances
Lengthy work zones
Use during long lines of traffic backup
Notes: Instructor should explain the need to have additional flaggers when there are side roads with in a work zone area

## Slide 233: Advanced or Additional Flagger Operations

## Slide 234
Except in emergency situations, Advanced Warning Signs must be in place prior to work taking place
Advanced Warning Signs
“Optional”
EPG 616.23.2.5.1 Signs & EPG 616.6.2
General Characteristics of Signs (MUTCD 6F.02)
Notes: Instructor should explain:
You cannot stage equipment or materials in the roadway until ALL signs are in properly in place and Flaggers have taking control of the roadway
These are the required signs that are to be used in both directions for flagging operations

## Slide 235
EPG 616.3.3
Components of Temporary Traffic Control Zones
(MUTCD 6C.03)

## Slide 236
Refer to the Engineering Policy Guide 616.8
Typical Applications
(MUTCD 6H)
Notes: Instructor should explain:
How to read the TA
The various components of the TA

## Slide 237: Advanced Warning
EPG 616.19.2.2.7 Sign Coverings
Signs must be removed or covered when not in use

## Slide 238: Channelizers
EPG 616.23.2.5.4 Channelizers & 616.6.63 Channelizing Devices (MUTCD 6F.63)
Trim Line
42 inches in height
Cone
28 inches in height
*For daytime operations on minor roads only

## Slide 239
Additional Traffic Control Devices to Consider

## Slide 240
LED Stop/Slow Paddle
2016 Innovations Showcase
Notes: LED Stop/Slow Paddles/signs: See attached vendor links
http://www.usa-sign.com/Library/VAWZSZStopSlow.pdf
Various signs/sizes, with flashing LED light assembly
http://www.tapconet.com/solar-led-division/flashing-led-paddle
http://www.xwalk.com/pages/stop-stop-LED-paddle.htm
https://www.grainger.com/product/TAPCO-Stop-Slow-LED-Paddle-Sign-3LCH4
http://www.truckntow.com/led-stop-slow-sign.html
http://sirennet.com/store/product/star-svp-tcs-1-led-slow-stop-traffic-control-sign
http://www.tapconet.com/store/product-detail/jaab/stop-slow-blinkerpaddle-flashing-led-paddles?c=Caab&sku=2180-00322

## Slide 241: Pilot Vehicle
Pilot vehicles are a safe and efficient means of moving traffic when a lane must be shared by traffic and the work zone area is lengthy or difficult to navigate
Two flaggers must be used when using a pilot vehicle
What are some advantages to using a pilot vehicle in a work zone during flagging operations?
Notes: Instructor should explain:
When pilot cars are used
The benefits to using pilot cars

## Slide 242: Pilot Vehicles
May be used to supplement flaggers.
  Control traffic speed through work zone
  Reduce confusion for motorist
  Reduce/eliminate property damage claims
Considerations:
  Traffic volume
  Length of lane closure
  Geometrics
  # of intersecting roads
  Turn around locations
  Type of work

## Slide 243: Automated Flagger Assistance Devices (AFAD)
Designed to be remotely operated
Positioned out of the lane of traffic
  Red/Yellow Lens AFAD shall alternately display a steadily illuminated CIRCULAR RED lens and a flashing CIRCULAR YELLOW lens
  Red/Yellow Lens AFAD shall include a gate arm
Notes: Instructor should explain:
When the AFAD can be used
The benefits to using AFAD’s rather than having actual people flagging

## Slide 244: Trailer Mounted Attenuator AFAD
Primary focus is to get flaggers off the road and out of traffic
Allows clearer direction to motorists by incorporating 3 color variable message boards, automated STOP/SLOW paddle, and flashing red/yellow signal
All TMA flagger operators shall be trained as a certified flagger with knowledge about the use of TMA flaggers
No part of the TMA flagger shall extend into the opposing lane
Shall follow the appropriate human flagging and AFAD TAs
TMA flagger in closed lane should be positioned at least 150 ft. in advance of the workspace
Shall be removed when not in use
Shall NOT be used for nighttime operations
Shall NOT be used for long-term stationary operations

## Slide 245: Portable Signal Flagging Device
May be used to control traffic movements in one-lane, two-way TTC zones
  Safety enhancement to the flaggers
Optional traffic control systems that may be used by contractor to replace flagging operations for short-term lane closures on two-lane highways
Requires 4 units with 2 units placed on either side of the roadway in each direction

## Slide 246
Long-term Rumble Strips
Short-term Rumble Strips
616.6.87 Temporary Rumble Strips (MUTCD 6F.87)
Notes: Instructor should explain:
How rumble strips are set up & where
Proper signing
Benefits to using rumble strips
When they should not be used
Temporary rumble strips should not be placed on:
Sharp horizontal or vertical curves.
Pedestrian crossings or on bicycle routes.
Roadways used by bicyclists unless a minimum clear path of 4 feet is provided at each edge of the roadway
Roadways when there are no workers present to monitor the rumble strips for possible shifting.
Examples of when temporary rumble strips may be beneficial include:
Flagging operations,
Lane closure on a multi-lane roadway or a work zone located on hilly or curved terrain which may have sight distance issues.

## Slide 247: Work Zone Inspections
Drive through your work zone once it is set up
Monitor compliance
Identify deficiencies
  Document deficiencies or any needed changes
  Take action
Photograph work zone
  Especially after an incident
EPG 616.19 Quality Standards for Temporary Traffic Control Devices
Notes: Instructor should explain:
The importance of Work Zone inspections
What to look for
The importance of documentation
What role new employees play in work zone inspections

## Slide 248: Protecting Yourself And Co-workers
Protect yourself and co-workers
Get vehicle and driver’s description
Do not leave your post
Stay focused and alert
In the event of an incident
Notes: REVIEW slide.
TRAINER’S TIP: Give an example of not leaving your post. For example: Vehicle stopped at flagger station. Another vehicle hit the first. Driver ran off. Flagger could not leave his post, except to move in front of the accident to flag around it.

## Slide 249
What Is Wrong With This?
Notes: Instructor should provide time to review each slide and ask the participants to list what they see wrong and why it is wrong.

## Slide 259: Review
Flaggers must: (check all that apply)
  Be mentally alert Have good sight and hearing
  Under the influence of drugs or alcohol Well rested
  Injured Confident
Flagging is not a job for:
  The crew leader C. Being confident
  Modified duty D. A supervisor
Flag paddles have a preferred height of at least _______ ft.
  3 C. 5
  12 D. 10
Flagger stations must be visible from at least _____ ft. during the day, and _____ ft. at night.
  500, 1,000 C. 250, 500
  500, 750 D. 1,000, 500
Flaggers should identify ________________ before beginning flagging procedures that day.
  A lunch spot C. Activities
  A flagging buddy D. An escape route

## Slide 260: Review Cont.
Flaggers should stand at least ________ from other workers, vehicles, or equipment.
  50 ft. C. 1 mile
  ½ mile D. 100 ft.
A flagger cannot be more than ________ from the flagger symbol sign.
  1 mile C. Being confident
  Modified duty D. A supervisor
Factors impacting glare include:
  Lighting unit set-up location C. Height of unit
  Direction lights are aimed D. All the above
Flaggers should not flag more than _____________.
  2 hours C. 15 minutes
  45 minutes D. 5 hours
There are ______________________ that flaggers use.
  Radios C. Hand signals
  Roads D. Flag paddles

## Slide 261: Review Cont.
Who has control over flagging operations?
  Lead flagger C. Crew leader
  Injured employees D. New employee
_____________ is the preferred communication tool used by flaggers.
  Hollering C. Text message
  Hand-held radio D. Pass the hat method
The ____________ tells traffic what to expect ahead.
  Termination area C. Channelizers
  Buffer Space D. Advanced warning area
The ________________ moves traffic out of its normal path.
  Channelizer C. Transition area
  Termination area D. Buffer space
A trim line must be ___________ in height.
  3-foot C. 1 foot
  48 inches D. 56 inches

## Slide 262: Review Cont.
_______________________ must be used when using a pilot vehicle.
  A lead flagger C. 2 flaggers
  A TMA D. Merging tapers
An ________________ is used to get flaggers off the roadway and out of traffic and can be operated remotely.
  Advance warning area C. Anchor
  AFAD D. Operator
A _____________________ is done to identify deficiencies in a work zone.
  Work zone inspection C. Crew member
  Channelizer D. TMA operator

## Slide 263: Group Project Stage 3

## Slide 264
Section 5: Work Zone Inspections

## Slide 265: Why Do Work Zone Inspections?
Safety for the worker and motorists
Monitor compliance
Identify deficiencies
Monitor the effectiveness of the traffic control plan
Improve future work zone plans
Notes: The work zone is too close to the barrier in the top picture.

## Slide 266: Inspections
Notes: Click on the forms in full screen. Forms are hyperlinked to the correct page for detail viewing. (internet required)
Hand out sample inspection forms to the class and explain the items that are looked at in a typical inspection.

## Slide 267: Work Zone Inspections
Two Inspection Categories
  Quality control inspections
  Quality assurance inspections

## Slide 268: Quality Control Inspections
Pre-installation
Post-installation
Routine
Removal
Notes: Quality Control Inspection performed by the project/operation MT supervisors, CM inspectors, and/or Contractors.
Pre-installation – are performed at a staging area or maintenance facility prior to deployment, these inspections ensure that the proper devices are available, in good condition, and working properly before being put into service. An inspection of the work zone area should not be overlooked during these inspections because modifications to the traffic control plan may be necessary to accommodate field conditions.
Post-installation – performed after the work zone plan has been deployed, used to ensure the proper set up, location of devices, devices are working properly, and the traffic is responding appropriately to the set up.
Routine – performed at regular intervals throughout the life of the work zone to identify any concerns in quality, performance, placement of devices, and traffic response.
Removal – performed upon the removal of devices from the work zone, the intent is to identify and complete any needed repairs and replacements before the devices are returned to inventory.

## Slide 269: Quality Assurance Inspections
Performed by Central Office engineering staff and District lead staff
More formal than QC inspections
Documented and shared results
Notes: Quality assurance inspections are conducted daily by Central Office and district staff. They cover 23 specific items pertaining to the visibility of work zones and 10 specific items pertaining to traffic flow through work zones. Central office traffic then reviews the ratings on a quarterly basis to determine where MoDOT is managing work zones well and where improvement is needed. Based on the results – new or refined guidelines, policies and standards are provided.
Explain that no equipment should be positioned before the first trimline and tapers should be clear
Picture on the left is acceptable that the vehicle is not in the taper while the picture on the right shows a vehicle within the taper.

## Slide 270: Quality Assurance Inspections
Technical inspections
Operational inspections
Notes: Technical inspections – focus on the physical aspects of the work zone, these inspections consist of identifying the temporary traffic control devices and measures present in a work zone and provides an objective evaluation of how well the work zone complies with MoDOT standards and specifications. For example, FHWA, Central Office, and District Personnel will team up and review 2-3 districts work zones per year and follow technical inspection criteria.
Operational inspections – focus on the more cognitive aspects of the work zone, these inspections strive to evaluate the work zone from the motorist’s perspective. MoDOT’s Temporary Traffic Control Inspection Worksheet and Temporary Traffic Control Visibility and Mobility Inspection Worksheet are examples inspectors use to perform technical and operational inspections, respectively. For example, District will form team to go around their districts and review work zone.

## Slide 271: Exposure
Can be seen as the number of people affected and the severity of the deficiencies
Good judgment must be used to determine the severity of exposures

## Slide 272: Priorities
To help determine the severity of an exposure the following categories should be used:
Priority 1
Priority 2
Priority 3
http://sp/sites/sm/IRPDocuments/Shared%20Documents/PUBLISHED/APPENDICES/AppendiceII%20-%20Incident%20Response%20Priorities.pdf
http://www.modot.mo.gov/business/standards_and_specs/Sec0616.pdf

## Slide 273: Priority 1
Deficiency presents an immediate hazard to the motorists or workers
Examples include:
  Improperly positioned flagger
  No PPE
  Blunt ends
  Missing devices
  Disabling glare
  Short tapers
Notes: Corrective actions should be taken ASAP (day or night, weekends or holidays) suspending other work if necessary. Failure to immediately address the problem can cause the operation to be shut down.
What’s wrong with this picture?

## Slide 274: Priority 2
Not an immediate threat but, can impact the proper functioning of the work zone.
Examples include:
  Missing pavement markings
  Improper spacing
  Traffic congestion
  Inappropriate speed limits
  Displaced/damaged devices
Notes: Corrective actions should be accomplished as soon as practical. Depending on the severity of the deficiency, they should be completed within 12 to 48 hours of notification.

## Slide 275: Priority 3
Doesn’t impact the functioning of the work zone but is more of a maintenance or aesthetic issue.
Examples include:
  Leaning signs
  Dirty devices
  Improper sign covering
  Improper PCMS message
  Intermixing devices
Notes: Corrective actions should be accomplished within 96 hours of notification.
Regardless of the severity of the deficiency, corrective actions should be made as soon as possible to maintain a quality work zone. Failure to do so could be grounds to suspend work.

## Slide 276: Review
What are the 2 categories of work zone inspections?
  Technical Quality Assurance
  Quality Control Operational
Priority ______ deficiencies present an immediate hazard to the motorists or workers.
  1 C. 2
  3
A priority ______ deficiency doesn’t impact the functioning of the work zone but is more of a maintenance or aesthetic issue.
  2 C. 3
  1

## Slide 277
Section 6: Safe Work Zone Removal Principals
Maintain Safety of Employees and the Traveling Public
Maximum Visibility
Safe and Controlled Flow of Traffic

## Slide 278: Work Zone Accident Statistics
Maintaining the Safety of the employees and the traveling public is a priority
In 2019, eighteen people were killed in work zones, compared to thirteen in 2018. Between 2015 and 2019, 65 people were killed, and 3,833 people were injured in Missouri work zones.
Since 2000, 19 MoDOT employees have been killed in the line of duty.
Notes: CDC

## Slide 279: Work Zone Accident Statistics Con’t.
The top five contributing circumstances for work zone crashes in 2019 were:
  Following too closely
  Improper lane use or changing lanes
  Inattention
  Failure to yield
  Driving too fast for conditions
The best defense in a work zone crash, or any crash, is a seat belt.
In 2019, 77 percent of vehicle occupant fatalities were not wearing a seat belt.
Notes: CDC

## Slide 280: What can you do to protect yourself and motorists?
Communicate to everyone what their role is
  Who is doing what
  Ask questions
Maintain maximum visibility
  What do you do if you have lost maximum visibility
Beware of blind spots
Regularly check your mirrors

## Slide 281: What can you do to protect yourself and motorists con’t.?
Control traffic through your work area
Proper TMA placement
  Be aware of
    Hill crests
    Blind curves
    Overhead signs and bridges
    On and off ramps

## Slide 282
Removing Work Zones
In some instances, it is recommended to pick up the work zone in reverse of set up
What are possible safety concerns?
  Trailer TMA’s
    Driver focuses on backing a trailer, no longer focusing on traffic or employees on the road
Notes: All TTC devices shall be removed as soon as practical when they are no longer needed. When work is suspended for short periods of time, TTC devices that are no longer appropriate shall be removed or covered.

## Slide 283
  How can you safely remove the remaining traffic control devices?
Notes:   Is it safe to walk behind the TMA and lead vehicle & arrow board to pick the remaining Devices up? Only thing between the crew and live traffic are a few devices. The lead vehicle is now behind the TMA. The answer is NO.

## Slide 284
A Safe Option
LEAVE advance warning signs in place
Leave shoulder taper and flashing arrow panel in place
Remove the lane taper
The work zone then transitions from a stationary operation to a signed mobile operation
  Employees on the ground are now in front of the Protective Vehicle/equipped with a TMA

## Slide 285
After the Traffic Control Devices are removed and the lane is open, the crew can safely circle around and remove the traffic control signs
The crews can retrieve the signs, shoulder taper, and flashing arrow panel on the right lane and then circle around to retrieve the left lane signs

## Slide 286: Review
The best defense in a work zone or any crash is a _________________.
  Air horn C. seatbelt
  Airbag D. Barricade
In some instances, it is recommended to pick up the work zone in ________________ of the set up for safety reasons.
  Reverse C. The same order
  Dark D. Winter
When removing the work zone, what devices should be left in place until the end of pick up?
  Lane taper Advance warning signs
  Shoulder taper Channelizers
  Flashing arrow panel

## Slide 287
Section 7: Post Work Zone Debriefing

## Slide 288
Have a post work zone debrief with the crew
Discuss the following:
  “Was the work zone safe?”
  “Can we do this safer?”
  Safety issues
  Traffic issues
  Route problems
  Equipment issues
  Coordination issues
  Personnel issues
  Interdepartmental cooperation
Speak Up & Share Information
What else can we do to be safe?
Notes: SAY: As we’ve said before, you help create the safety culture by sharing info and speaking up when you don’t think something is safe.

## Slide 289: Sharing Information
Morning Meeting
Risk Based Analysis (RBA)
Innovations Challenge
Notes: SAY: Earlier in the week I’m sure you heard about ways we share information to keep us safe. Your building should have a morning meeting to discuss and plan the jobs for the day. Also, a Risk Based Analysis (RBA) is done on each job/process to plan ahead to be safe. Lastly, if you have an idea on how to be safer or any other innovation, fill out an Innovations challenge submission form. See you supervisor or mentor for more information.

## Slide 290: So We Go Home Safe
Notes: Say: This should be the ultimate goal every day at MoDOT. To accomplish this it requires buy-in from every employee. Have the attitude that we rely on one another as TEAMMATES to make sure we go home safely everyday

## Slide 291: Test Time!

## Slide 292
Final Discussions & Questions
Notes: Overall Review.