## Slide 1
Topcon Magnet Field
March 2024

## Slide 2
Job
Configure
Exchange
Edit
Calculate
Map
Connect
Setup
Survey
Stake
Reports
Apps
Topcon Magnet Field

## Slide 3
Configure
Survey
Coord Sys
Global
Backup
Units
Display
Alarms
Stake Reports
Enterprise
Topcon Magnet Field

## Slide 4
Global
MAGNET Field software interface parameters and options applied through all the jobs.
Main Tab
Theme Tab
Job Tab
Shared Data Tab
Keyboard Tab
Topcon Magnet Field

## Slide 5
Global Settings (Main)
Enable Job History
  stores the field measurements on the job to the jobhistory.xml file.
Custom MyDocuments folder
  defines the location of custom folder for data storage
Topcon Magnet Field

## Slide 6
Global Settings (Theme)
Use Bold Font check box to display the text in bold font style
Full Screen check box to switch in full screen mode.
Button Sound check box to enable sound effects when you click any functional button. (Deselecting “Button Sound” recommended)
Topcon Magnet Field

## Slide 7
Global Settings (Job)
Localization:
  Select Never import to create new jobs without importing localization.
  Select Always import to automatically import localization.
  Select Prompt to import to choose every time if you want to import localization.
Topcon Magnet Field

## Slide 8
Global Settings (Job)
Global Code Library:
  Select Never import to create new jobs without importing global codes.
  Select Always import to automatically import global codes.
  Select Prompt to import to choose every time if you want to import global codes.
Topcon Magnet Field

## Slide 9
Global Settings (Job)
mmGPS Settings:
  Select Never import to create new jobs without importing mmGPS settings.
  Select Always import to automatically import mmGPS settings.
  Select Prompt to import to choose every time if you want to import mmGPS settings.
Topcon Magnet Field

## Slide 10
Global Settings (Job)
Backsight Setup:
  Select Never import to create new jobs without importing backsight setup settings.
  Select Always import to automatically import backsight setup settings.
  Select Prompt to import to choose every time if you want to import backsight setup settings.
Topcon Magnet Field

## Slide 11
Global Settings (Job)
Quick Codes:
  Select Never import to create new jobs without importing quick codes.
  Select Always import to automatically import quick codes.
  Select Prompt to import to choose every time if you want to import quick codes.
Topcon Magnet Field

## Slide 12
Global Settings - Job
Base Estimation:
  Select Never import to create new jobs without importing base estimation data.
  Select Always import to automatically import base estimation data.
  Select Prompt to import to choose every time if you want to import base estimation data.
Topcon Magnet Field

## Slide 13
Global Settings - Job
Continue Point Name Numbering
  check box affects an automatically suggested name of the first point added to a new job. If the check box is selected, the point naming will continue from the last open job.
  Example: the name of the final point in previous job is "84"; the increment value is "9"; the name of the new job’s start point will be "93".
Topcon Magnet Field

## Slide 14
Global Settings - Shared Data
The Shared Data File field displays the current file (*.mxl / *.mxlzip / *.xml / *.gc3) used to provide shared data to the current job.
FC5000/6000 Shared Data File path...C:\Users\MODOT\ Documents\MAGNET Field PC
Topcon Magnet Field

## Slide 15
Global Settings - Shared Data
Check the Use Control Points box to use points in the shared data file as external control points in the current job without importing them.
Topcon Magnet Field

## Slide 16
Global Settings - Shared Data
Check the Use Code Library box to use codes from the shared data file in the current job.
Topcon Magnet Field

## Slide 17
Global Settings (Shared Data)
Manage Shared Data button adds data from the current job to the currently selected shared data file or delete data from the currently selected shared data file. Points and codes are supported.
Create Shared Data button creates a new shared data file (supported formats: *.mxl / *.mxlzip).
Topcon Magnet Field

## Slide 18
Global Settings (Keyboard)
MAGNET Keyboard check box to enable typing with the on-screen keyboard. It displays automatically when editing values.
Topcon Magnet Field

## Slide 19
Live Demonstration
Topcon Magnet Field

## Slide 20
Units
Setting different units and precisions for how MAGNET Files will display various numerical values in dialogs.
Distance
Angle
Coordinate
Other
Topcon Magnet Field

## Slide 21
Units (Distance)
Distance Unit for any length values. This can be…
  US Feet
  Meters
  IFeet (International Feet)
Currently using…US Feet
If the units are US Feet, linear values can be entered as meters or international feet by appending “m” or “if” to the entered value.
Topcon Magnet Field

## Slide 22
Units (Distance)
Distance Precision for the number of decimal places in length values.
Rover poles are typically graduated to the nearest centimeter, so we recommend setting distance precision to….0.123
Topcon Magnet Field

## Slide 23
Units (Distance)
Area Unit for area values. This can be…
  Sq. Meters
  Sq. Ifeet
  Sq. USFeet
Typically, we use…Square US Feet
Topcon Magnet Field

## Slide 24
Units (Distance)
Volume Unit for volume values. This can be…
  Cubic Meters
  Cubic IFeet
  Cubic US Feet
  Cubic IYards
  Cubic USYards
Typically, we use…Cubic USYards
Topcon Magnet Field

## Slide 25
Units (Angle)
Meas Angle Unit for values of the measured values. This can be…
  DMS – degrees minutes seconds
  DD.ddddd - decimal degrees
  Grads (Gons) – gradians
Typically, we use…DMS
Topcon Magnet Field

## Slide 26
Units (Angle)
Meas Angle Precision for the number of decimal places in angular values.
Typically, we use…0°00’00”
Topcon Magnet Field

## Slide 27
Units (Angle)
Calc Angle Unit for angular values in Calculation tasks. In addition to Angular Unit settings, that also can be…
  Radians
  (full circle = 2*PI radians)
  Mils
  (1 Mil = 1 Milliradians = 1/1000 of a Radian)
Topcon Magnet Field

## Slide 28
Units (Angle)
Calc Angle Precision for the number of decimal places in angular values in Calculation tasks.
Typically, we use…0°00’00”
Topcon Magnet Field

## Slide 29
Units (Coordinate)
Northing/Easting Precision for the number decimal places in Northing/Easting Coordinates.
Recommend 0.123 or 0.1234
Topcon Magnet Field

## Slide 30
Units (Coordinate)
Lat/Lon Units for the specifying of Latitude and Longitude format.
Always…DD°MM’SS.s
Topcon Magnet Field

## Slide 31
Units (Coordinate)
Lat/Lon Units for the number of decimal places in latitude/longitude seconds.
Always…0°00’00.12345
Topcon Magnet Field

## Slide 32
Units (Coordinate)
Height Precision for the number of decimal places in ellipsoid height and elevations.
Always…0.123
Topcon Magnet Field

## Slide 33
Units (Other)
Temperature Unit only used for raw measurements.
  Celsius (°C)
  Fahrenheit (°F)
Topcon Magnet Field

## Slide 34
Units (Other)
Pressure Unit only used for raw measurements.
  mmHg…(millimeters of Mercury)
  inHg…(inches of Mercury) 1 inHg = 33.8639 mbar
  hPa…(hectoPascals)
  mbar…(millibar) 1 mbar = 0.02953 inHg
  1 bar = 1000 millibar
Topcon Magnet Field

## Slide 35
Live Demonstration
Topcon Magnet Field

## Slide 36
Display
Use for customizing the displaying of values in the job.
Display Options….
Coordinate Type
Plane Coordinate Order
Geodetic Azimuth Origin
Direction
Display Slope As
Station Prefix
CL Position
Topcon Magnet Field

## Slide 37
Display
Coordinate Type displays coordinates for the coordinate system type selected.
Grid…e.g., Missouri State Plane
Datum (Lat/Lon/Ell ht)…e.g. (NAD83 Lat/Lon/Ellipsoid Ht)
Datum (Lat/Lon/Elevation)…e.g. (NAD83 Lat/Lon/Elevation)
WGS84 (Lat/Lon/Ell ht)
WGS84 (Lat/Lon/Elevation)
Datum (Xc/Yc/Zc)
WGS84 (Xc/Yc/Zc)
Topcon Magnet Field

## Slide 38
Display
Plane Coordinate Order displays the Cartesian system order representing the position relative to a local origin.
Typically displayed in controller as…North, East, Height
Topcon Magnet Field

## Slide 39
Display
Geodetic Azimuth Origin displays the azimuth computed from reference direction.
Always set to…North
Topcon Magnet Field

## Slide 40
Display
Direction displays the directions as bearings or azimuth.
Typically set to…Bearing
Topcon Magnet Field

## Slide 41
Display
Display Slope As sets how the slope will be displayed and specified: as gradient.
Typically set to…Bearing
Topcon Magnet Field

## Slide 42
Display
Station Prefix selects the desired format for station naming by picking a prefix from the drop-down list.
The button opens the dialog where you can edit existing and create your own prefix for station.
Typically set to…Sta.
Topcon Magnet Field

## Slide 43
Display
CL Position select a desired format to display stationing the centerline.
1234.00…Chainage, the distance to the station along the centerline.
12+34.000…US Station (American format), when using 100 units as a full station plus a remainder.
1+234.000…EU Station (Euro Station) aka “Metric”, when using 1000 units as a full station and a slash before a remainder.
Always set to…12+34.000
Topcon Magnet Field

## Slide 44
Live Demonstration
Topcon Magnet Field

## Slide 45
Coordinate System
Coordinate System in geometry, is a is a system that uses one or more numbers, or coordinates, to uniquely determine the position.
Projection
Use Grid/Ground
Datum
Geoid Model
Topcon Magnet Field

## Slide 46
Coordinate System
Projection in surveying are methods used to transform the spherical surface of the earth into a two-dimensional plane.
next to the Projection dialog, opens the Pre-Defined CS dialog and allow user to add desired projections to the list of projection in the current job.
Select the SPC83 projection/s specific to your district region.
Topcon Magnet Field

## Slide 47
Coordinate System
Missouri State Plane Coordinate Zones
Topcon Magnet Field

## Slide 48
Coordinate System (Use Grid/Ground)
Use Grid/Ground enables transformation to ground coordinates for surveying. After applying the coordinate system with selected Use Grid/Ground, the coordinates system in the current job will be ground
Grid/Ground Parameters
Configure BEFORE importing data
Parameters – Scale Factor
Combined SF – Projection Factor
Direction – Grid to Ground
Topcon Magnet Field

## Slide 49
Coordinate System (Datum)
Datum (horizontal) is a specified coordinate system for a collection of positions on the surface of the earth.
Datum…NAD83_NO_TRANS
Topcon Magnet Field

## Slide 50
Coordinate System (Datum)
Geoid Model is the physical reference surface of the earth. Its shape reflects the distribution of mass inside the Earth. Geoid undulations are important for converting GNSS-derived ellipsoidal height differences to orthometric height difference (elevations).
opens the geoid list dialog and allow user to add desired geoid to the list of projection in the current job.
Current Geoid Model…Geoid18
Topcon Magnet Field

## Slide 51
Live Demonstration
Topcon Magnet Field

## Slide 52
Codes
Used to configure code, quick code and control code settings in the job.
Topcon Magnet Field

## Slide 53
Codes Options (Quick Codes)
Allows the user to simplify and speed up adding necessary codes to surveyed points by setting quick code groups.
opens the Quick Codes Group (QCG) dialog, allows user to add desired quick code groups.
Topcon Magnet Field

## Slide 54
Codes Options (Quick Codes)
Multiple Code assignment for each Quick Code Group.
Topcon Magnet Field

## Slide 55
Codes Options (Quick Codes)
QCG are semi-transparent buttons displayed on a survey map.
Each button has its own set of point codes assigned to it.
Clicking any of these buttons during the survey and it measures a point in Quick mode and automatically applies assigned code(s) to a stored point.
Topcon Magnet Field

## Slide 56
Live Demonstration
Topcon Magnet Field

## Slide 57
Stake Reports
Report provides detailed information regarding the observation parameters and results of the stake out location compared the to design location.
To create and to manage configurations of stakeout reports.
Topcon Magnet Field

## Slide 58
Stake Reports (Stake Reports Config List)
MAGNET Field supports five predefined types of stake reports and offers default configurations for each of them.
Line/Arc
Point
Road
Slope
Surface
Topcon Magnet Field

## Slide 59
Stake Reports (Report Config)
User can create new configurations or copy, edit, or delete existing configurations for any type of stake reports. Each type of stake reports supports multiple configurations for various job tasks.
Topcon Magnet Field

## Slide 60
Live Demonstration
Topcon Magnet Field

## Slide 61
Survey
Job Configurations
  GNSS Base/Rover
  GNSS MoDOT Network
  Total Station
  Hybrid Integration (GNSS/RTS)
Topcon Magnet Field

## Slide 62
Job Configuration
Optical Configuration
  Manual Total Station (MTS)
  Robotic Total Station (RTS)
GNSS Configuration
  GNSS Base/Rover
  GNSS MoDOT Network
  Hybrid Integration (GNSS/RTS)
Topcon Magnet Field

## Slide 63
Configuration Library (GNSS)
Creating a GNSS Profile
  GR-3_Base/Rover
  HiPer VR_Base/Rover
  HiPer HR_Base/Rover
Topcon Magnet Field

## Slide 64
Configuration
Name (antenna) Base/Rover
  Ex: GR-3_Base/Rover
  Ex: HiPer VR_Base/Rover
Type is RTK
Topcon Magnet Field

## Slide 65
Receiver Make
Set both Rover and Base Manufacturer to…Topcon
Topcon Magnet Field

## Slide 66
Base Receiver
Receiver model…GR-3, HiPer VR
Serial Number…optional
Elevation mask…13 degrees
RTK Format…
  GR3…RTCM 3.x
  HiPer VR and HR…RTCM 3.x
Antenna Height (ARP Location)
  Vertical (2m Fixed tripod)
  Slant (standard tripod)
Topcon Magnet Field

## Slide 67
Base Radio
Type…Internal Radio
Model
  GR-3…Digital UHF or Digital UHF II
  HiPer VR and HR…R2 Lite UHF
Port…C
Baud…115200 (standard)
Topcon Magnet Field

## Slide 68
Base Radio Parameters
Power…1 W
Protocol…PDL
Modulation
  GR-3…GMSK
  HiPer V, HR, VR…4SFK
Scrambling…ON
Forward Error Correction (FEC)…ON
Topcon Magnet Field

## Slide 69
Rover Receiver
Receiver model…GR-3, HiPer VR
Serial Number…optional
Elevation mask…13 degrees
RTK Format…
  GR3…RTCM 3.x
  HiPer VR and HR…RTCM 3.x MSM3
Antenna Height
  Vertical (2m Fixed tripod)
Topcon Magnet Field

## Slide 70
Rover Radio
Type…Internal Radio
Model
  GR-3…Digital UHF or Digital UHF II
  HiPer VR and HR…R2 Lite UHF
Port…C
Baud…115200 (standard)
Note: Base and Rover radio settings must match to communicate between receivers.
Topcon Magnet Field

## Slide 71
Rover Radio Parameters
Protocol…PDL
Modulation
  GR-3…GMSK
  HiPer V, HR, VR…4SFK
Scrambling…ON
Forward Error Correction (FEC)…ON
Note: Base and Rover radio settings must match to communicate between receivers.
Topcon Magnet Field

## Slide 72
Topo Survey
Precise – used for collecting observations on project control
  Solution – Fixed Only
  Average – establishes the number of epochs collected during an observation… 180 minimum
  Precision (USft) – establishes a Horiz. and Vert. precision threshold on measurements
    HRMS…0.0492
    VRMS…0.0984
Topcon Magnet Field

## Slide 73
Topo Survey
Advanced Epoch Filtering –
Precision (USft) – establishes a Horiz. and Vert. precision threshold on measurements
    HRMS…XXXX
    VRMS…XXXX
Topcon Magnet Field

## Slide 74
Topo Survey
SureTopo Settings –
Precision (USft) - establishes a Horiz. and Vert. precision threshold on measurements
    Hor. Tolerance…XXXXX
    Vert. Tolerance…XXXXX
    Num. of Matches…XXXXX
Quick – establishes a Horiz. and Vert. precision threshold on measurements
    Hor. Tolerance…XXXXX
    Vert. Tolerance…XXXXX
    Num. of Matches…XXXXX
Topcon Magnet Field

## Slide 75
Topo Survey
Quick – used for collecting observations on planimetric and topographic features, and control check observation
  Solution – Fixed Only
  Average – establishes the number of epochs collected during an observation…3 or 5 minimum
  Precision (USft) – establishes a Horiz. and Vert. precision threshold on measurements…Uncheck
Topcon Magnet Field

## Slide 76
Auto Topo Survey
Solution-Fixed Only
Method
  By Time
  By Horizontal Distance
  By Slope Distance
  By Elevation
  By Stop and Go
Interval
Topcon Magnet Field

## Slide 77
Stake Settings
Horizontal Distance Tolerance – determines when close enough to the point for the bull’s eye to appear.
Vertical Distance Tolerance - determines when close enough to the point for the bull’s eye to appear.
Compass Orientation – top of screen is oriented to the North during stakeout session
Display Reference -
Topcon Magnet Field

## Slide 78
Stake Settings
Quick – used for collecting observations on planimetric and topographic features, and control check observation
  Solution – Fixed Only
  Average – establishes the number of epochs collected during an observation…3 or 5 minimum
  Precision (USft) – establishes a Horiz. and Vert. precision threshold on measurements…Uncheck
Topcon Magnet Field

## Slide 79
Grade Stake Marking
Working stake length– Enter the length of the stake
Top Spacing-Top space reserved for marking
Bottom Spacing-Bottom space reserved for marking
Cut/Fill Interval- Even number that you want the cut/Fill rounded to
Topcon Magnet Field

## Slide 80
Stake Point Icon- Define how staked points will be displayed on map
Icon- Select what special icon you want displayed
Use Tolerance Colors- A checked box allows you to choose color based on inside or outside distance tolerance
Color-Allows you to choose color of icon
Topcon Magnet Field

## Slide 81
Point Naming
Prefix/Suffix-can be added to point name
Name as-You can use Design point, Next stake point, Design pt. Prefix, Design pt. suffix, Design pt. + Constant, or Range start
Note-You can choose Design Point, Design pt. prefix, Design pt. suffix, Station & Offset, or none
Topcon Magnet Field

## Slide 82
Tracking
Current constellations used in US; GPS, Glonass, Beidou, and Galileo
GR 3 – GPS+GLO only
HiPer V – GPS+GLO only
Hyper VR – GPS+GLO+BDS+GAL
Hyper HR - GPS+GLO+BDS+GAL
  (Only if receiver has been upgraded)
Topcon Magnet Field

## Slide 83
Advanced
RTK Position-Extrapolation or Matched Epoch.
Base Sat Limit-can set number of satellites to transmit from base. Uncheck
Multipath Reduction-helps reduce multipath. Leave checked
Canopy Environment-????
Topcon Magnet Field

## Slide 84
RTK Settings
Topcon Magnet Field

## Slide 85
RTK Settings
Set Fix Level to Medium
Topcon Magnet Field

## Slide 86
Topcon Magnet Field

## Slide 87
Miscellaneous
Prompt for antenna height- ask for height before point is stored
Stakeout sound- indicates the point is staked
Beep on storing points- beeps each time a point is stored. On by default
Topcon Magnet Field

## Slide 88
Configuration Library (Network RTK)
Create a GR-3 Network Rover
Topcon Magnet Field

## Slide 89
Configuration
Name
Type
Corrections
Protocol
Topcon Magnet Field

## Slide 90
Rover Receiver
Receiver Model
Elevation Mask
Antenna Details
  Slant
  Vertical
Topcon Magnet Field

## Slide 91
Rover Radio
Controller
Topcon Magnet Field

## Slide 92
Internet Address
Setting up a connection to MoDOT Real Time Network
Topcon Magnet Field

## Slide 93
Edit Internet Address
Label- just a name
Address- rtk3.modot.mo.gov
Login- insert your username
Password- insert your password
Topcon Magnet Field

## Slide 94
Internet Address
Topcon Magnet Field

## Slide 95
Position in GGA
Check Automatic Rover Position
Tells RTN where you are so that it can create correction stream
Topcon Magnet Field

## Slide 96
Topo Survey
Precise
  Average 180
  Check on Precision
Quick
  Average 3
Topcon Magnet Field

## Slide 97
Auto Topo Survey
Solution-Fixed Only
Method
  By Time
  By Horizontal Distance
  By Slope Distance
  By Elevation
  By Stop and Go
Interval
Topcon Magnet Field

## Slide 98
Stake Settings
Horizontal Distance Tolerance
Vertical Distance Tolerance
Compass Orientation
Display Reference
Topcon Magnet Field

## Slide 99
Stake Settings
Precise
Quick
Topcon Magnet Field

## Slide 100
Grade Stake Settings
Topcon Magnet Field

## Slide 101
Staked Point Icon
What your staked point will look like on screen
Topcon Magnet Field

## Slide 102
Point Naming
If you store a point when staking
Topcon Magnet Field

## Slide 103
Tracking
GR-3-Glonass only
Hyper V- Glonass only
Hyper VR-Glonass, BDS, and Galileo
Hyper HR- Glonass, BDS, and Galileo (As long as it has been upgraded)
Topcon Magnet Field

## Slide 104
Advanced
RTK Position
  Extrapolation
Topcon Magnet Field

## Slide 105
RTK Settings
Topcon Magnet Field

## Slide 106
RTK Settings
Set Fix Level to Medium
Topcon Magnet Field

## Slide 107
Topcon Magnet Field

## Slide 108
Miscellaneous
Personal Preferences
Topcon Magnet Field

## Slide 109
Live Demonstration
Topcon Magnet Field

## Slide 110
Live Demonstration
Topcon Magnet Field

## Slide 111
Topcon Magnet Field
Job
New Job
Open Job
Delete Job
Job Info
Job Photos
Save Job As
Copy Job
Create Job from File

## Slide 112
Topcon Magnet Field
New Job
Name
Created By…(optional)
  Recommend entering person creating job file.
Comments…(optional)
  Recommend entering description for job file.
Current Date…(system clock)

## Slide 113
Topcon Magnet Field
Job Configuration
Optical Configuration
GNSS Configuration

## Slide 114
Topcon Magnet Field
Configuration Library
Optical Configuration
  Conventional…GTS 4, 500, 600, 700 Series
  Robotic…GT 1000 or GT 1200 Series
  Motorized…GTS 800 Series

## Slide 115
Topcon Magnet Field
Configuration Library
GNSS Configuration
  HiPer VR_Base/Rover
  HiPer VR_Network
  GR 3_Base/Rover
  GR 3_Network
  GT 1003/1203_Hybrid

## Slide 116
Coordinate System
Coordinate System
  Projection
  Datum
  Geoid Model
Projection
  Zone Selection
  Use Grid/Ground
Topcon Magnet Field

## Slide 117
Coordinate System
Grid/Ground Parameters
  Must be configured BEFORE importing data…control, align
  Parameters – Scale Factor
  Combined SF – Projection Factor
  Direction – Grid to Ground
Datum
  NAD83_NO-TRANS
Geoid Model
  g2018u7 current Geoid model
Topcon Magnet Field

## Slide 118
Shared Data
MoDOT codes
  MoDOT_yyyy-mm-dd.mxl
Topcon Magnet Field

## Slide 119
Units (Distance)
Distance Unit
  US Feet
Distance Precision
  0.12 or 0.123
Area Unit
  Square US Feet
Volume Unit
  Cubic US Feet
Topcon Magnet Field

## Slide 120
Units (Angle)
Meas Angle Unit
  DMS
Meas Angle Precision
  0°00’00”
Calc Angle Unit
  DMS
Calc Angle Precision
  0°00’00”
Topcon Magnet Field

## Slide 121
Units (Coordinate)
Northing/Easting Precision
  0.1234
Lat/Lon Units
  DD°MM’SS.s”
Lat/Lon Precision
  0°00’00.12345”
Height Precision
  0.123
Topcon Magnet Field

## Slide 122
Units (Other)
Temperature Unit
  Fahrenheit (°F)
Pressure Unit
  mmHg…(millimeters of Mercury)
  inHg…(inches of Mercury) 1 inHg = 33.8639 mbar
  hPa…(hectoPascals)
  mbar…(millibar) 1 mbar = 0.02953 inHg
  1 bar = 1000 millibar
Topcon Magnet Field

## Slide 123
Units (Other)
Temperature Unit
  Fahrenheit (°F)
Pressure Unit
  mmHg…(millimeters of Mercury)
  inHg…(inches of Mercury) 1 inHg = 33.8639 mbar
  hPa…(hectoPascals)
  mbar…(millibar) 1 mbar = 0.02953 inHg
  1 bar = 1000 millibar
Topcon Magnet Field

## Slide 124
Live Demonstration
Topcon Magnet Field

## Slide 125
Open Job
Default Location
Browse
  Navigation to alternate location
Topcon Magnet Field

## Slide 126
Delete Job
Default Location
Browse
  Navigation to alternate location
Warning…Last Chance!
Topcon Magnet Field

## Slide 127
Live Demonstration
Topcon Magnet Field

## Slide 128
Exchange
To Job
From Job
To File
From File
Enterprise
Topcon Magnet Field

## Slide 129
Exchange
To Job
From Job
To File
From File
Enterprise
Topcon Magnet Field

## Slide 130
Live Demonstration
Topcon Magnet Field

## Slide 131
Edit
Points
Codes
Layers
Linework
Areas
Point Lists
Raw Data
Background
Surfaces
Planes
Roads
Topcon Magnet Field

## Slide 132
Edit (Points)
Points
Topcon Magnet Field

## Slide 133
Edit (Areas)
Areas
Topcon Magnet Field

## Slide 134
Edit (Points Lists)
Point Lists
Add Point List
  Name…point list
  Add…points
Add
  Selection Parameters
Modification
  Delete
  Edit
Topcon Magnet Field

## Slide 135
Edit (Surfaces)
Surfaces
Topcon Magnet Field

## Slide 136
Edit (Roads)
Surfaces
Topcon Magnet Field

## Slide 137
Live Demonstration
Topcon Magnet Field

## Slide 138
Calculate
Inverse
Calculator
Curves
Area
Angles
Offsets
Surfaces
Topcon Magnet Field

## Slide 139
Live Demonstration
Topcon Magnet Field

## Slide 140
Inverse
Pt to Pt
Calculator
Curves
Area
Angles
Offsets
Surfaces
Topcon Magnet Field

## Slide 141
Live Demonstration
Topcon Magnet Field

## Slide 142
Map
Map Properties
Calculator
Curves
Area
Angles
Offsets
Surfaces
Topcon Magnet Field

## Slide 143
Live Demonstration
Topcon Magnet Field

## Slide 144
Connect
XXXXXXX
Topcon Magnet Field

## Slide 145
Live Demonstration
Topcon Magnet Field

## Slide 146
Setup
Status
Manage Receiver
Localization
Start Base
Simulator
Topcon Magnet Field

## Slide 147
Status (Setup)
Status dialog contains information about current survey, connected receiver position and satellite constellations. The status information is presented in the following tabs:
Position Tab
System Tab
Multi Base Status Tab
Scatter Plots Tab
SVs Tab
Log History Tab
Topcon Magnet Field

## Slide 148
Position Tab (Status)
Position Tab – displays the data related to a currently occupied position.
icon displays the number of satellites tracked
icon displays the number of satellites used in position determination
Local Time, Solution type, Coordinates
PDOP…Position Dilution of Precision
HRMS and VRMS, the RMS values
Base Distance
Topcon Magnet Field

## Slide 149
System Tab (Status)
Position Type…Autonomous, Float, and Fixed
GPS, GLO, SBAS, QZSS, GAL, BDS, and NAVIC constellations
Radio Link…quality of radio link
RTK-Age(sec)…age of last correction message
Topcon Magnet Field

## Slide 150
System Tab (Status)
Receiver Storage…available memory in the receiver for storing TPS files
Internal Battery…remaining battery charge of the internal
Removeable Battery…HiPer HR
Ext Battery Pack…GR3/GR5
External Power…12v battery
Controller…Storage and power
Network…Datum and Grid
Topcon Magnet Field

## Slide 151
Scatter Plot (Status)
Displays graphically the current receiver position changing in time and showing measurements scatter.
Topcon Magnet Field

## Slide 152
Scatter Plot (Status)
Represents graphically the satellites on the sky and their signal-to-noise ratio (SNR).
Topcon Magnet Field

## Slide 153
Live Demonstration
Topcon Magnet Field

## Slide 154
Manage Receiver (Setup)
Manage GNSS receiver settings, file management and firmware.
DO NOT recommend non-experienced users in these tools
CADD Support or Dealer should assist with updating firmware and receiver configurations within the Manage Receiver Tools.
Topcon Magnet Field

## Slide 155
Manage Receiver (Setup)
Info…dialog displays information about the receiver's model, firmware, ID, serial number, and OAF expiration date. In this dialog you can send Clear NVRAM command to the GNSS receiver.
File Manager…dialog displays a list of files stored in internal memory of the GNSS receiver and allows a user to download, upload and remove files in GNSS receiver.
Topcon Magnet Field

## Slide 156
Manage Receiver (Setup)
OAF License…dialog displays information about loaded licensed options and allows a user uploading the new OAF.
Update…Allows a user to upload a firmware to the connected receiver.
Recovery…Allows a user to recovery a receiver via a its serial port.
Settings…Allows a user to configure receiver's miscellaneous settings.
WiFi…Allows a user to configure and manage the Wi-Fi module in a receiver that supports this connectivity (NET G5, HiPer HR, etc.).
Topcon Magnet Field

## Slide 157
Live Demonstration
Topcon Magnet Field

## Slide 158
Survey
Topo
Auto Topo
X-Section
Find Station
Tape Dim.
Surface
Topcon Magnet Field

## Slide 159
Topo Survey (GNSS)
To collect points with the GNSS rover receiver by determining coordinates of locations on the survey site and storing points at the user's command
Topcon Magnet Field

## Slide 160
Topo Survey (GNSS)
Normal view - displays real-time coordinates for the current position, provides an editable overview of the point being stored, contains point and GNSS raw data saving tools, and shows feedback on GNSS receiver activity.
Map view - shows the surveying process in real time on the map and contains point and GNSS raw data saving tools including buttons with quick codes.
Topcon Magnet Field

## Slide 161
Topo Survey (GNSS)
GNSS Precise Mode – click to determine coordinates of the current position in GNSS Precise Mode. Then click to accept determined coordinates and save the point to the job.
Topcon Magnet Field

## Slide 162
Topo Survey (GNSS)
GNSS Quick Mode – click to determine coordinates of the current position in GNSS Quick Mode. Command will auto save the point to the job.
Topcon Magnet Field

## Slide 163
Topo Survey (GNSS)
Map View– switch to Map View to visually overview the current position and the positions of possible reference objects.
Topcon Magnet Field

## Slide 164
Topo Survey (GNSS)
– to access some on-the-fly tools and GNSS status tool
- to access the GNSS solution requirements for saving points can be changed at any time.
Topcon Magnet Field

## Slide 165
Auto Topo (GNSS)
Auto Topo survey allows you to collect points automatically.
While the GNSS rover receiver obtains the required GNSS solution, MAGNET Field checks the status of the criterion in real time and saves the obtained coordinates as another auto topo point in the job at the moment the criterion condition is met.
Topcon Magnet Field

## Slide 166
Auto Topo Survey (GNSS)
Store Criteria
Solution
  Fixed Only
Method
  By Time
  By Horiz Dist
  By Slope Dist
  By Elevation
  Stop and Go
Interval
Topcon Magnet Field

## Slide 167
Live Demonstration
Topcon Magnet Field

## Slide 168
Live Demonstration
Topcon Magnet Field

## Slide 169
Stake
XXXXXXX
Topcon Magnet Field

## Slide 170
Stake Point (Stake)
To stake design points. MAGNET Field supports points stacking in several modes – standard mode, PTL (point to line), and Drape
Typically, we use…Standard Mode
Topcon Magnet Field

## Slide 171
Stake Point (Stake)
To stake a point, select either Design Point or the Nearest Point
If the Design Point is selected, entered manually or select from map or from the list of job points.
If the Nearest Point is selected, MAGNET Field will automatically look for a nearest point among existing points in the current job.
Toggle between Design Point and Nearest Point, select the button next to the hand icon
Topcon Magnet Field

## Slide 172
Live Demonstration
Topcon Magnet Field

## Slide 173
Lines (Stake)
To stake points along the line formed by design points.
If the Design Point is selected, entered manually or select from map or from the list of job points.
If the Nearest Point is selected, MAGNET Field will automatically look for a nearest point among existing points in the current job.
Toggle between Design Point and Nearest Point, select the button next to the hand icon
Topcon Magnet Field

## Slide 174
Stake Point (Stake)
To stake a point, select either Design Point or the Nearest Point
If the Design Point is selected, entered manually or select from map or from the list of job points.
If the Nearest Point is selected, MAGNET Field will automatically look for a nearest point among existing points in the current job.
Toggle between Design Point and Nearest Point, select the button next to the hand icon
Topcon Magnet Field

## Slide 175
Live Demonstration
Topcon Magnet Field

## Slide 176
Reports
Field Reports
Stake Reports
DL Reports
Report Header
Topcon Magnet Field

## Slide 177
Live Demonstration
Topcon Magnet Field

## Slide 178
Apps
Take Photo
Photo Viewer
Files
Topcon Magnet Field

## Slide 179
Take Photo (Apps)
Starts camera application or opens the Capture dialog to take a photo.
Use the buttons to zoom in- , zoom out – , or reset zoom –
To capture the photo, click the button. The Preview dialog opens after capturing to confirm saving to the current job.
Topcon Magnet Field

## Slide 180
Photo Viewer (Apps)
Starts pictures and video browser to view pictures attached to the current job.
Topcon Magnet Field

## Slide 181
Files (Apps)
Starts file explorer to manage files.
Topcon Magnet Field

## Slide 182
Live Demonstration
Topcon Magnet Field